## Slide 3: Objectives
Provide a detailed overview of the C64x+/C674x CPU architecture
Describe the basic ASM language and h/w needed to solve a SOP
Analyze how the hardware pipeline works
Learn basics of software pipelining

## Slide 4: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 5: What Problem Are We Trying To Solve?
Digital sampling of an analog signal:
A
t
Most DSP algorithms can be expressed with MAC:
count
i = 1
Y =  coeffi * xi
for (i = 0; i < count; i++){ Y += coeff[i] * x[i]; }
DAC
x
Y
ADC
DSP
How is the architecture designed to maximize computations like this?
Notes: Over the next 20 slides, we want to provide an example to anchor the presentation and provide context. What better algorithm than the standard sum-of products. The question lead-in is “so, what problem are we trying to solve?” “The basics of DSP involve first sampling an analog signal and converting it to digital. What do we do then? Some type of algorithm to shape, modify, etc the signal. This is easily done in the digital realm. So, the time between samples is our limit to how fast we need to do the algorithm. What’s a typical algorithm look like - this! A simple sum-of products. Let’s look at a typical DSP algorithm and see how the processor is designed to handle it.
Spend about 1 minute on this slide. If the group is VERY new to DSP, you might embellish slightly on any areas you feel comfortable with. But remember, the focus is not WHY DSP, it is “assuming you know why you’d want to use this algorithm, let’s see how the processor is built to handle it”.
The lead-into the next slide is the Q shown on the slide. Also state that we plan to write the code for this algorithm and see how the architecture is designed to handle it efficiently.
OLD INFO

## Slide 6: 'C6x CPU Architecture
Memory
‘C6x Compiler excels at Natural C
Multiplier (.M) and ALU (.L) provide up to 8 MACs/cycle (8x8 or 16x16)
Specialized instructions accelerate intensive, non-MAC oriented calculations. Examples include:
Video compression, Machine Vision, Reed Solomon, …
While MMACs speed math intensive algorithms, flexibility of 8 independent functional units allows the compiler to quickly perform other types of processing
‘C6x CPU can dispatch up to eight parallel instructions each cycle
All ‘C6x instructions are conditional allowing efficient hardware pipelining
A0
A31
. .
.S1
.D1
.L1
.S2
.M1
.M2
.D2
.L2
B0
B31
. .
Controller/Decoder
MACs
Note: More details later…

## Slide 7: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 8: The Core of DSP : Sum of Products
Mult
ALU
MPY c, x, prod
ADD y, prod, y
y =
40
cn xn
n = 1
*
The ‘C6000
Designed to handle DSP’s math-intensive calculations
ALU
.M
MPY .M c, x, prod
.L
ADD .L y, prod, y
Note:
You don’t have to specify functional units (.M or .L)
Where are the variables stored?
Notes: Here are the two basic operations (mpy, add) written in linear assembly. The architecture contains two functional units which perform these two basic operations.
  .M does multiply.
  .L does add. (Why .L? It actually stands for ALU, but since “A” is used for something else, they chose to use “L”; we’ll describe this “A” thing next).
Leading Question (to next foil):
Where do you think the variables (c, x, Y, etc) are stored?
Side Note:
We’ve chosen to use linear asm because of it’s simple format. We’ll expand on the other coding methods later. We suggest you don’t get into these at this point of the presentation.

## Slide 9: Working Variables : The Register File
y =
40
cn xn
n = 1
*
Register File A
c
x
prod
32-bits
y
. . .
.M
.L
16 or 32 registers
MPY .M c, x, prod
ADD .L y, prod, y
How can we loop our ‘MAC’?
Notes: Where do we keep the variables?
In “A” register file (ha, ha).
Like all good RISC processors, the ‘C6000 is a load/store machine.
All data is loaded to and stored from registers. Then the execute units only operate on data found within the CPU.
Side Note:
If they ask about how to do loads and stores, tell them we’ll get to that in a minute (after creating a loop). It was too late to rearrange the presentation.

## Slide 10: Making Loops
1. Program flow: the branch instruction
2. Initialization: setting the loop count
3. Decrement: subtract 1 from the loop counter
B loop
SUB cnt, 1, cnt
MVK 40, cnt
Notes: In keeping with the RISC concept, our loop is managed by three instructions
<they come up in sequence with transitions>.
  1. Branch (conditional)
  2. A counter set to the number of iterations we need.
  3. A means to decrement the counter.
In DSPs, classically, hardware is dedicated to watching the counter. But that increases h/w complexity, and remember, h/w control -- is a barrier to high speeds (faster clock rates).

## Slide 11: “.S” Unit: Branch and Shift Instructions
y =
40
cn xn
n = 1
*
MVK .S 40, cnt
loop:
MPY .M c, x, prod
ADD .L y, prod, y
SUB .L cnt, 1, cnt
B .S loop
.M
.L
.S
Register File A
32-bits
c
x
prod
y
. . .
cnt
How is the loop terminated?
16 or 32 registers
Notes: Here we add in the counter and decrement it within each loop.
Leading Question to next foil ...
Is that all we need for the loop? Oh yeah, we need to make the Branch conditional. That is, when our counter reaches zero, we want to exit the loop.
VelociTI -- again -- uses s/w rather than h/w in order to maintain h/w simplicity.
So, right -- you guessed it. We have an instruction for this, too

## Slide 12: Conditional Instruction Execution
Note: If condition is false, execution is essentially replaced with nop
Code Syntax Execute if:
[ cnt ] cnt  0 [ !cnt ] cnt = 0
Execution based on [zero/non-zero] value of specified variable
To minimize branching, all instructions are conditional
[condition] B loop
Notes: Every instruction can be conditional. This works great for the branch instruction, but it also works well for other instructions (i.e. conditional loads or stores, etc.).
When, using a hardware pipelined processor to reach these speeds, branches cause latency in program execution. We created 100% conditional instructions … in order to reduce the number of branches (or breaks in the program flow).
Side Note:
This really is beneficial for pipelined architectures. Which of course is required to get the speeds of the ‘C6000 today (and even more so, in the future).

## Slide 13: Loop Control via Conditional Branch
y =
40
cn xn
n = 1
*
MVK .S 40, cnt
loop:
MPY .M c, x, prod
ADD .L y, prod, y
SUB .L cnt, 1, cnt
[cnt] B .S loop
.M
.L
.S
Register File A
32-bits
c
x
prod
y
. . .
cnt
How are the c and x array values brought in from memory?
16 or 32 registers
Notes: Here we add in the counter and decrement it within each loop.
Leading Question to next foil ...
Is that all we need for the loop? Oh yeah, we need to make the Branch conditional. That is, when our counter reaches zero, we want to exit the loop.
VelociTI -- again -- uses s/w rather than h/w in order to maintain h/w simplicity.
So, right -- you guessed it. We have an instruction for this, too

## Slide 14: Memory Access via “.D” Unit
.M
.L
.S
y =
40
cn xn
n = 1
*
MVK .S 40, cnt
loop:
LDH .D *cp , c
LDH .D *xp , x
MPY .M c, x, prod
ADD .L y, prod, y
SUB .L cnt, 1, cnt
[cnt] B .S loop
Data Memory:
x(40), a(40), y
Register File A
c
x
prod
y
cnt
*cp
*xp
*yp
.D
What does the “H” in LDH signify?
16 or 32 registers
Note: No restrictions on which regs can be used for address or data!
Notes: . Here we used “LDH” since we chose halfword (short) data types. Only LD/ST can use POINTERS !!
And look … we added a new functional unit “.D” for data moves.
On the next iteration through the loop, do we want to be pointing to the same data value (in my input arrays)? No, we want to increment the pointer to the next value.
How do you increment something in C? You use “++”. We do the same thing here.

## Slide 15: Memory Access via “.D” Unit
.M
.L
.S
y =
40
cn xn
n = 1
*
MVK .S 40, cnt
loop:
LDH .D *cp , c
LDH .D *xp , x
MPY .M c, x, prod
ADD .L y, prod, y
SUB .L cnt, 1, cnt
[cnt] B .S loop
Data Memory:
x(40), a(40), y
Register File A
c
x
prod
y
cnt
*cp
*xp
*yp
.D
How do we increment through the arrays?
16 or 32 registers
Instr. Description C Type Size
LDB load byte char 8-bits
LDH load half-word short 16-bits
LDW load word int 32-bits
LDDW* load double-word double 64-bits
* Except C62x & C67x generations
Notes: Default – loads into the low part of the 32-bit register file. Want it in the high half? Load/shift.
And look … we added a new functional unit “.D” for data moves.
On the next iteration through the loop, do we want to be pointing to the same data value (in my input arrays)? No, we want to increment the pointer to the next value.
How do you increment something in C? You use “++”. We do the same thing here.

## Slide 16: Auto-Increment of Pointers
Register File A
c
x
prod
y
cnt
*cp
*xp
*yp
y =
40
cn xn
n = 1
*
MVK .S 40, cnt
loop:
LDH .D *cp++, c
LDH .D *xp++, x
MPY .M c, x, prod
ADD .L y, prod, y
SUB .L cnt, 1, cnt
[cnt] B .S loop
.M
.L
.S
Data Memory:
x(40), a(40), y
.D
How do we store results back to memory?
16 or 32 registers
Notes: . Here we used “LDH” since we chose halfword (short) data types.
And look … we added a new functional unit “.D” for data moves.
On the next iteration through the loop, do we want to be pointing to the same data value (in my input arrays)? No, we want to increment the pointer to the next value.
How do you increment something in C? You use “++”. We do the same thing here.

## Slide 17: Storing Results Back to Memory
Register File A
c
x
prod
y
cnt
*cp
*xp
*yp
y =
40
cn xn
n = 1
*
MVK .S 40, cnt
loop:
LDH .D *cp++, c
LDH .D *xp++, x
MPY .M c, x, prod
ADD .L y, prod, y
SUB .L cnt, 1, cnt
[cnt] B .S loop
STW .D y, *yp
.M
.L
.S
Data Memory:
x(40), a(40), y
.D
But wait - that’s only half the story...
16 or 32 registers
Notes: . Here we used “LDH” since we chose halfword (short) data types.
And look … we added a new functional unit “.D” for data moves.
On the next iteration through the loop, do we want to be pointing to the same data value (in my input arrays)? No, we want to increment the pointer to the next value.
How do you increment something in C? You use “++”. We do the same thing here.

## Slide 18: Dual Resources : Twice as Nice
A0
A1
A2
A3
A4
Register File A
A15
or
A31
A5
A6
A7
cn
xn
prd
sum
cnt
. .
*c
*x
*y
.M1
.L1
.S1
.D1
.M2
.L2
.S2
.D2
Register File B
B0
B1
B2
B3
B4
B15
or
B31
B5
B6
B7
. .
32-bits
. .
. .
32-bits
Our final view of the sum of products example...
Notes: For those of you who’ve seen the architecture before, you’ve already realized that this was only HALF the story…we actually have DOUBLE of everything!
With 8 functional units you can execute up to 8 instructions/cycle. At 4ns (or 5ns) per cycle, we’re really zooming …
Just think of what you can do with all this … and how fast it’ll go!

## Slide 19: Optional - Resource Specific Coding
MVK .S1 40, A2
loop: LDH .D1 *A5++, A0
LDH .D1 *A6++, A1
MPY .M1 A0, A1, A3
ADD .L1 A4, A3, A4
SUB .S1 A2, 1, A2
[A2] B .S1 loop
STW .D1 A4, *A7
y =
40
cn xn
n = 1
*
A0
A1
A2
A3
A4
Register File A
A15
or
A31
A5
A6
A7
cn
xn
prd
sum
cnt
. .
*c
*x
*y
.M1
.L1
.S1
.D1
32-bits
. .
It’s easier to use symbols rather than
register names, but you can use
either method.
Notes: Our code is now complete.
We’ve shown linear assembly thus far so you can see the ‘C6000 VelociTI architecture at work. TI’s Assembly optimizer takes linear ASM and creates standard asm code as shown here.
You can program the ‘C6000 in three ways:
  1. C
  2. Linear Asm
  3. Standard Asm
Most people choose C or linear asm because of their simple, symbolic methodology.
Leading question to next foil ...
Looking closer at this diagram, where did the 1’s come from (in the unit specification? (As in .S1, .M1, …?)

## Slide 20: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 21: ‘C62x RISC-like instruction set
.L
.D
.S
.M
No Unit Used
IDLE
NOP
.S Unit
NEG NOT OR SET SHL SHR SSHL SUB SUB2 XOR ZERO
ADD ADDK ADD2 AND B CLR EXT MV MVC MVK MVKH
.L Unit
NOT OR SADD SAT SSUB SUB SUBC XOR ZERO
ABS ADD AND CMPEQ CMPGT CMPLT LMBD MV NEG NORM
.M Unit
SMPY SMPYH
MPY MPYH MPYLH MPYHL
.D Unit
NEG STB (B/H/W) SUB SUBAB (B/H/W) ZERO
ADD ADDAB (B/H/W) LDB (B/H/W) MV
Notes: We won’t take the time to go through each one of these instructions. Notice, though, that some instructions can be performed on multiple functional units.
This foil shows the 56 base instructions of the ‘C62x. A small, but powerful set!
Leading comment for next foil …
The ‘C67x has all these same instructions, plus ...
HANDOUT: Instruction Set by category.

## Slide 22: ‘C67x: Superset of Fixed-Point
.L
.D
.S
.M
No Unit Required
IDLE
NOP
.S Unit
NEG NOT OR SET SHL SHR SSHL SUB SUB2 XOR ZERO
ADD ADDK ADD2 AND B CLR EXT MV MVC MVK MVKH
ABSSP ABSDP CMPGTSP CMPEQSP CMPLTSP CMPGTDP CMPEQDP CMPLTDP RCPSP RCPDP RSQRSP RSQRDP SPDP
.L Unit
NOT OR SADD SAT SSUB SUB SUBC XOR ZERO
ABS ADD AND CMPEQ CMPGT CMPLT LMBD MV NEG NORM
ADDSP ADDDP SUBSP SUBDP INTSP INTDP SPINT DPINT SPRTUNC DPTRUNC DPSP
.M Unit
SMPY SMPYH
MPY MPYH MPYLH MPYHL
MPYSP MPYDP MPYI MPYID
.D Unit
NEG STB (B/H/W) SUB SUBAB (B/H/W) ZERO
ADD ADDAB (B/H/W) LDB (B/H/W) LDDW MV
Notes: And ‘C6701 Floating Point uses a super set of this same instruction set.
This is further evidence of the similarity of the ‘C62x and ‘C67x devices.
Two things to point out with the ‘C67x instructions:
  The ‘C67x is the first DSP processor (if not microprocessor) to provide Double-Precision floating-point hardware! The ‘C67x has hardware that performs either single-precision (SP) or double-precision (DP) floating-point math.
  The ‘C67x also includes double-precision integer multiplication. That is, you can do 32x32 bit multiplication and get a 64-bit result.

## Slide 23: 'C64x: Superset of ‘C62x Instruction Set
.L
Data Pack/Un PACK2 PACKH2 PACKLH2 PACKHL2 PACKH4 PACKL4 UNPKHU4 UNPKLU4 SWAP2/4
Dual/Quad Arith ABS2 ADD2 ADD4 MAX MIN SUB2 SUB4 SUBABS4
Bitwise Logical ANDN
Shift & Merge SHLMB SHRMB
Load Constant MVK (5-bit)
.D
.S
.M
Bit Operations BITC4 BITR DEAL SHFL
Move MVD
Average AVG2 AVG4
Shifts ROTL SSHVL SSHVR
Multiplies MPYHI MPYLI MPYHIR MPYLIR MPY2 SMPY2 DOTP2 DOTPN2 DOTPRSU2 DOTPNRSU2 DOTPU4 DOTPSU4 GMPY4 XPND2/4
Mem Access LDDW LDNW LDNDW STDW STNW STNDW
Load Constant MVK (5-bit)
Dual Arithmetic ADD2 SUB2
Bitwise Logical AND ANDN OR XOR
Address Calc. ADDAD
Data Pack/Un PACK2 PACKH2 PACKLH2 PACKHL2 UNPKHU4 UNPKLU4 SWAP2 SPACK2 SPACKU4
Dual/Quad Arith SADD2 SADDUS2 SADD4
Bitwise Logical ANDN
Shifts & Merge SHR2 SHRU2 SHLMB SHRMB
Compares CMPEQ2 CMPEQ4 CMPGT2 CMPGT4
Branches/PC BDEC BPOS BNOP ADDKPC
Notes: This foil doesn’t need much introduction. The ‘C67x includes all the ‘C62x instructions along with these additional instructions.
Those that end in SP are for single-precision floating-point; those in DP are for double-precision floating-point. The ‘C67x is the only DSP (if not only microprocessor) with hardware support for double-precision.

## Slide 24: C64x+ Additions
.L
ADDSUB
ADDSUB2
DPACK2
DPACKX2
SADDSUB
SADDSUB2
SHFL3
SSUB2
.D
.S
.M
CMPY
CMPYR
CMPYR1
DDOTP4
DDOTPH2
DDOTPH2R
DDOTPL2
DDOTPL2R
GMPY
MPY2IR
MPY32 (32-bit result)
MPY32 (64-bit result)
MPY32SU
MPY32U
MPY32US
SMPY32
XORMPY
None
CALLP
DMV
RPACK2
DINT
RINT
SPKERNEL
SPKERNELR
SPLOOP
SPLOOPD
SPLOOPW
SPMASK
SPMASKR
SWE
SWENR
None
Notes: This foil doesn’t need much introduction. The ‘C67x includes all the ‘C62x instructions along with these additional instructions.
Those that end in SP are for single-precision floating-point; those in DP are for double-precision floating-point. The ‘C67x is the only DSP (if not only microprocessor) with hardware support for double-precision.

## Slide 25: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 26: DOTP2 with LDDW
=
+
a2
a0
A1:A0
LDDW .D1 *A4++,A1:A0
|| LDDW .D2 *B4++,B1:B0
A2
B2
a3*x3 + a2*x2
a1*x1 + a0*x0
DOTP2 A0,B0,A2
|| DOTP2 A1,B1,B2
+
intermediate sum
ADD A2,A3,A3
a1
a3
:
A5
x2
x0
B1:B0
x1
x3
:
final sum
ADD A3,B3,A4
A4
+
|| ADD B2,B3,B3
intermediate sum
A3
B3
Notes: All of these instructions can work in parallel. This is just an example of what the instructions look like and how they work.

## Slide 27: Block Real FIR Example (DDOTPL2 )
for (i = 0; I < ndata; i++) {
sum = 0;
for (j = 0; j < ncoef; j++) {
sum = sum + (d[i+j] * c[j]);
}
y[i] = sum;
}
loop Iteration [i,j] | [0,0] | [0,1]
 | d0c0 + d1c1 | 
 |  | d1c0 + d2c1
 | d2c2 | 
 | d3c3 | d3c2
 | . . . | 
Four 16x16 multiplies
In each .M unit every cycle
--------------------------------------
adds up to 8 MACs/cycle, or
8000 MMACS
Bottom Line: Two loop iterations for the price of one
DDOTPL2 d3d2:d1d0, c1c0, sum1:sum0

## Slide 28: Complex Multiply (CMPY)
 | A0 | r1 |  | i1 |  |  |  |  |  |  |  | 
 |  | x |  | x |  |  |  |  |  |  |  | 
 | A1 | r2 |  | i2 |  |  |  |  |  |  |  | 
 |  | = |  | = |  |  |  |  |  |  |  | 
 | CMPY A0, A1, A3:A2 | r1*r2 - i1*i2 |  |  |  | : |  | i1*r2 + r1*i2 |  |  |  | 
 |  |  | 32-bits |  |  |  |  |  | 32-bits |  |  | 
Four 16x16 multiplies per .M unit
Using two CMPYs, a total of eight 16x16 multiplies per cycle
Floating-point version (CMPYSP) uses:
  64-bit inputs (register pair)
  128-bit packed products (register quad)
  You then need to add/subtract the products to get the final result
single .M unit

## Slide 29: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 30: C66x: QMPY32 (fixed), QMPYSP (float)
 | A3:A2:A1:A0 | c3 | : | c2 | : | c1 | : | c0 | 
 |  | x |  | x |  | x |  | x | 
 | A7:A6:A5:A4 | x3 | : | x2 | : | x1 | : | x0 | 
 |  | = |  | = |  | = |  | = | 
 | A11:A10:A9:A8 | c3*x3 | : | c2*x3 | : | c1*x1 | : | c0*x0 | QMPY32
 |  |  |  |  |  |  |  |  | or QMPYSP
 |  | 32-bits |  | 32-bits |  | 32-bits |  | 32-bits | 
Four 32x32 multiplies per .M unit
Total of eight 32x32 multiplies per cycle
Fixed or floating-point versions
Output is 128-bit packed result (register quad)
single .M unit

## Slide 31: C66x: Complex Matrix Multiply (CMAXMULT)
src1 | r1 | i1 | : | r2 | i2 |  |  |  |  |  |  | 
 | src2_3 |  |  | src2_2 |  |  | src2_1 |  |  | src2_0 |  | 
src2 | ra | ia | : | rb | ib | : | rc | ic | : | rd | id | 
dest | r1*ra - i1*ia + r2*rc - i2*ic |  | : | r1*ia + i1*ra + r2*ic + i2*rc |  | : | r1*rb - i1*ib + r2*rd - i2*id |  | : | r1*ib + i1*rb + r2*id + i2*rd |  | 
single .M unit
32-bits
32-bits
32-bits
32-bits
Single .M unit implements complex matrix multiply using 16 MACs (all in 1 cycle)
Achieve 32 16x16 multiplies per cycle using both .M units
[ M9 M8 ] | = | [ M7 M6 ] | * | M3 M2 M1 M0
M9 = M7*M3 + M6*M1
M8 = M7*M2 + M6*M0
Where Mx represents a packed 16-bit complex number

## Slide 32: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 33: Pipeline Phases
Pipeline Full
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
PG PS PW PR DP DC E1
Program Fetch
Execute
Decode
Notes: Review again, plus a lead in Q (#cyc to execute?). This always causes a little controversy in the workshop, but controversy and discussion is sometimes a good thing (get ‘em worked up, a little red, a few tears, some fruit flying across the room, a few people calling 1-800-Analog-Devices, then we bring them back to reality…toy with ‘em, bait ‘em, they’re engineers, they’ll “byte” on anything…). Sorry - got carried away again. The sadistic side of me surfaces from time to time <grin>.
If they don’t know the answer, I typically ask: “what would you WANT it to be?” One cycle (or less!)

## Slide 34: Pipeline Phases
Full Pipe
Notes: Review again, plus a lead in Q (#cyc to execute?). This always causes a little controversy in the workshop, but controversy and discussion is sometimes a good thing (get ‘em worked up, a little red, a few tears, some fruit flying across the room, a few people calling 1-800-Analog-Devices, then we bring them back to reality…toy with ‘em, bait ‘em, they’re engineers, they’ll “byte” on anything…). Sorry - got carried away again. The sadistic side of me surfaces from time to time <grin>.
If they don’t know the answer, I typically ask: “what would you WANT it to be?” One cycle (or less!)

## Slide 35: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 36: Instruction Delays
Single Cycle 0
Multiply 1
Load 4
Branch B 5
All, instr’s except ...
MPY, SMPY
LDB, LDH, LDW
Description # Instr. Delay
All 'C64x instructions require only one cycle to execute, but some results are delayed ...
Notes: Here’s where the controversy stems from. First we state that all instructions require one cycle to execute (E1), but some results of the instruction are delayed. Now, some people say “bah humbug - you’re lying”, but it’s true. The point we are subtly making here is that, for example, a load instruction does not tie up the D unit for a total of 5 cycles - it only ties it up for one pipeline cycle (E1). On the next cycle, you could begin a new load. This is a “way of looking at it” as well as - it’s the truth. It also points them (kinda) in the direction of software pipelining (gee, I can do another load on the next cycle…etc). This is actually a test question, so they’ll get the point even if you or the students miss it here.
So, the first msg is: think about every instr executing in one cycle - but some results are delayed. The next key point is - a majority of the instructions DO execute and have no results delayed in ONE cycle. The next point is: there are only three classes of instructions (and they’re easy to remember) that have delays: multiply, load, branch.
Now, I don’t typically call these “delay slots” yet - we “delay” that discussion until later. It’s enough just to say that the results of these instructions (like getting a value from memory for a load) are delayed x cycles.

## Slide 37: Would This Code Work As Is ??
MVK .S1 40, A2
loop: LDH .D1 *A5++, A0
LDH .D1 *A6++, A1
MPY .M1 A0, A1, A3
ADD .L1 A4, A3, A4
SUB .S1 A2, 1, A2
[A2] B .S1 loop
STW .D1 A4, *A7
y =
40
cn xn
n = 1
*
A0
A1
A2
A3
A4
Register File A
A15
or
A31
A5
A6
A7
cn
xn
prd
sum
cnt
. .
*c
*x
*y
.M1
.L1
.S1
.D1
32-bits
. .
Need to add NOPs to get this code to work properly…
NOP = “Not Optimized Properly”
How many instructions can this CPU execute every cycle?
Notes: Our code is now complete.
We’ve shown linear assembly thus far so you can see the ‘C6000 VelociTI architecture at work. TI’s Assembly optimizer takes linear ASM and creates standard asm code as shown here.
You can program the ‘C6000 in three ways:
  1. C
  2. Linear Asm
  3. Standard Asm
Most people choose C or linear asm because of their simple, symbolic methodology.
Leading question to next foil ...
Looking closer at this diagram, where did the 1’s come from (in the unit specification? (As in .S1, .M1, …?)

## Slide 38: Software Pipelined Algorithm
.L1
.L2
.S1
.S2
.M1
.M2
.D1
.D2
add
mpy3
mpy2
mpy
7
6
5
4
3
2
1
0
ldw8
ldw7
ldw6
ldw5
ldw4
ldw3
ldw2
ldw m
ldw8
ldw7
ldw6
ldw5
ldw4
ldw3
ldw2
ldw n
1
4
mpyh3
mpyh2
mpyh
sub7
sub6
sub5
sub4
sub3
sub2
sub
add
B6
B5
B4
B3
B2
B
2
7
5
8
LOOP
PROLOG
3
6
Notes: 52

## Slide 39: Software Pipelined ‘C6x Code
c0: ldw .D1 *A4++,A5
|| ldw .D2 *B4++,B5
c1: ldw .D1 *A4++,A5
|| ldw .D2 *B4++,B5
|| [B0] sub .S2 B0,1,B0
c2_3_4: ldw .D1 *A4++,A5
|| ldw .D2 *B4++,B5
|| [B0] sub .S2 B0,1,B0
|| [B0] B .S1 loop
.
.
.
c5_6: ldw .D1 *A4++,A5
|| ldw .D2 *B4++,B5
|| [B0] sub .S2 B0,1,B0
|| [B0] B .S1 loop
|| mpy .M1x A5,B5,A6
|| mpyh .M2x A5,B5,B6
.
.
*** Single-Cycle Loop
loop: ldw .D1 *A4++,A5 || ldw .D2 *B4++,B5 || [B0] sub .S2 B0,1,B0 || [B0] B .S1 loop || mpy .M1x A5,B5,A6 || mpyh.M2x A5,B5,B6 || add .L1 A7,A6,A7 || add .L2 B7,B6,B7
Notes: 53

## Slide 40: Outline
What Does A DSP Do?
CPU – From the Inside – Out…
Instruction Sets
“MAC” Instructions
C66x – “MAC” Instructions
Hardware Pipeline
Software Pipelining
Chapter Quiz

## Slide 41: Chapter Quiz
Name the four functional units and types of instructions they execute:
How many 16x16 MACs can a C674x CPU perform in 1 cycle? C66x ?
Where are CPU operands stored and how do they get there?
What is the purpose of a hardware pipeline?
What is the purpose of s/w pipelining, which tool does this for you?

## Slide 42: Chapter Quiz
Name the four functional units and types of instructions they execute:
How many 16x16 MACs can a C674x CPU perform in 1 cycle? C66x ?
Where are CPU operands stored and how do they get there?
What is the purpose of a hardware pipeline?
What is the purpose of s/w pipelining, which tool does this for you?
M unit – Multiplies (fixed, float)
L unit – ALU – arithmetic and logical operations
S unit – Branches and shifts
D unit – Data – loads and stores
C674x – 8 MACs/cycle, C66x – 32 MACs/cycle
Register Files (A and B), Load (LDx) data from memory
Maximize performance – use as many functional units as possible in every cycle, the COMPILER/OPTIMIZER performs SW pipelining
To break up instruction execution enough to reach min cycle count thereby allowing single cycle execution when pipeline is FULL

## Slide 44: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal