## Slide 3: Objectives
Compare/contrast different uses of memory (internal, external, cache)
Define cache terms and definitions
Describe C6000 cache architecture
Demonstrate how to configure and use cache optimally
Lab 14 – modify an existing system to use cache – benchmark solutions

## Slide 4: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 5: Parking Dilemma
Parking Choices:
0 minute walk @ $100 for close-in parking
Sports
Arena
Close Parking
0 minute walk
10 spaces
$100/space
Distant Parking-Ramp
10 minute walk
10 minute walk
1000 spaces
$5/space
Parking Choices:
0 minute walk @ $100 for close-in parking
10 minute walk @ $5 for distant parking
Parking Choices:
0 minute walk @ $100 for close-in parking
10 minute walk @ $5 for distant parking
or …

## Slide 6: Parking Dilemma
Sports
Arena
Distant Parking-Ramp
10 minute walk
10 minute walk
1000 spaces
$5/space
Parking Choices:
0 minute walk @ $100 for close-in parking
10 minute walk @ $5 for distant parking
or …
Valet parking: 0 minute walk @ only $6.00
How does this compare to cache memory?
Close Parking
0 minute walk
10 spaces
$100/space

## Slide 7: Why Cache?
Sports
Arena
Bulk Memory
Fast
Memory
Memory Choices:
Small, fast memory
Large, slow memory
Memory Choices:
Small, fast memory
Large, slow memory
or …
Slower
Larger
Cheaper
Fast
Small

## Slide 8: Why Cache?
Sports
Arena
Bulk Memory
Cache
Memory
Slower
Larger
Cheaper
Memory Choices:
Small, fast memory
Large, slow memory
or … Use Cache:
Combines advantages of both
Like valet, data movement is automatic
Fast
Small
Works like Big, Fast Memory

## Slide 9: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 10: Using Cache Memory
CPU
Cache
Cache H/W
External Memory
EMIF
Program
func1
func2
func3
0x8000
Cache hardware automatically transfers code/data to internal memory, as needed
Addresses in the Memory Map are associated with locations in cache
Cache locations do not have their own addresses
Let’s start with Basic Concepts of a Cache …
Notes: When using the internal memory as memory-mapped RAM, you can either copy all your tasks (or at least the critical ones) into internal memory and execute as needed.
Some systems even “overlay” tasks, that is, they have the DMA copy in new programs threads (routines) while executing others. In this way they can be available as they’re needed. This is often done when the entire program code cannot fit on chip all-at-once.
Of course, if it seems like all your DMA bandwidth is spent copying program code into the internal program memory, you could instead enable the cache. Why? Because this is exactly what a cache is for. It automatically stores program code into internal memory as it is used. Then it’ll be available on-chip whenever it’s needed again. Since most DSP code consists of many loops, this is a great solution.
The cache keeps track of what’s in internal memory and when it runs out of internal memory, it dumps the oldest stuff. AND, it does all this without using any of your DMA channels. Cool!

## Slide 11: Cache: Block, Line, Index
External Memory
0x8000
Conceptually, a cache divides the entire memory into blocks equal to its size
A cache is divided into smaller storage locations called lines
The term Index or Line-Number is used to specify a specific cache line
0x8010
0x8020
 |  | Cache
 | 0 | 
 | . . . | 
 | 0xF | 
Block
Cache
Line
Index
How do we know which block is cached?

## Slide 12: Cache Tags
External Memory
0x8000
A Tag value keeps track of which block is associated with a cache block
Each line has its own tag -- thus, the whole cache block won’t be erased when lines from different memory blocks need to be cached simultaneously
0x8010
0x8020
Tag | Index | Cache
800 | 0 | 
801 | 1 | 
 | . . . | 
 | 0xF | 
How do we know a cache line is valid (or not)?

## Slide 13: Valid Bits
External Memory
0x8000
A Valid bit keeps track of which lines contain “real” information
They are set by the cache hardware whenever new code or data is stored
0x8010
0x8020
Tag | Index | Cache
800 | 0 | 
801 | 1 | 
 | . . . | 
721 | 0xF | 
Valid |  | 
 | 1 | 
 | 1 | 
 | . . . | 
 | 0 | 
 | 0 | 
This type of cache is called ...

## Slide 14: Direct-Mapped Cache
External Memory
0x8000
0x8010
0x8020
 | Index | Cache
 | 0 | 
 | . . . | 
 | 0xF | 
Block
Direct-Mapped Cache associates an address within each block with one cache line
Thus … there will be only one unique cache index for any address in the memory-map
Only one block can have information in a cache line at any given time
Let's look at an example ...

## Slide 15: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 16: Direct-Mapped Cache Example
External Memory
0x8000
0x8010
0x8020
0x8030
Index
Tag
3 0
15 4
Tag | Index | Cache
 | 0 | 
 | 1 | 
 | . . . | 
 | E | 
 | 0xF | 
Let’s examine an arbitrary direct-
mapped cache example:
A 16-line, direct-mapped cache requires a 4-bit index
If our example P used 16-bit addresses, this leaves us with a 12-bit tag
Valid |  | 

## Slide 17: Arbitrary Direct-Mapped Cache Example
The following example uses:
  16-line cache
  16-bit addresses, and
  Stores one 32-bit instruction per line
C6000 cache’s have different cache and line sizes than this example
It is only intended as a simple cache example to reinforce cache concepts
Notes: Let’s look at an example. It’s hard to understand exactly how the cache works from talking about its address components.
PLEASE NOTE TO THE STUDENTS THAT THIS IS A CONCEPTUAL EXAMPLE!
For foil-space (and time) limitations, this example:
- cache’s instructions rather than fetch packets
- only has a 16-bit address rather than 26
- simply breaks the imaginary 16-bit address into a 12-bit tag and 4 bit index

## Slide 18: Conceptual Example Code
0003h
0004h
0005h
0006h
0026h
0027h
0028h
L1 LDH
MPY
ADD
B L2
L2 ADD
SUB cnt
[!cnt] B L1
Code
Address
Tag
Index
15 4 3 0
Notes: Here’s the code for our example -- once again, note the 16-bit address, 12-bit tag, and 4-bit index.

## Slide 19: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
Cache
Tag
Valid
Notes: Here’s what our imaginary cache looks like. The cache has a full instruction (remember we usually cache FP’s).
Also, we have our tag memory.
Finally, there is one additional valid bit for each cache line. This indicates whether that particular line is valid or not.

## Slide 20: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
Cache
Tag
Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: Is the first instruction in cache?

## Slide 21: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
Cache
Tag
Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: No. If you look at the index of the “sub: LDH” instruction, you’ll notice the valid bit is not set for index=3.
Since the value is not found in the cache, this is called a “cache miss”.

## Slide 22: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
Cache
Tag
Valid
Compulsory Miss
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1

## Slide 23: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
Cache
000
Tag

Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: So, the data memory controller goes off-chip for the program code and brings it back to the CPU and the cache. The cache inserts the instruction, saves the tag value, and sets the valid bit.

## Slide 24: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
Cache
000
000
Tag


Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 25: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
Cache
000
000
000
Tag



Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 26: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B
Cache
000
000
000
000
Tag




Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 27: Direct Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD
Cache
000
000
000
000 002
Tag




Valid
Conflict Miss
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: Notice, this time the valid bit was set, but the tag was wrong. This time when the memory controller brings the new instruction on chip, it must over-write the cache and tag locations.
In a one-way direct-mapped cache, there can only be one instruction (i.e. fetch packet) for given index value. (Note, you’ll see the ‘C6211 allows up to a 4-way cache in level-2 memory, this means you can have up to 4 fetch packets per index).

## Slide 28: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD
SUB
Cache
000
000
000
000 002
002
Tag





Valid
Address | Code
0003h | L1 LDH
0004h | MPY
0005h | ADD
0006h | B L2
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 29: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD
SUB
B
Cache
000
000
000
000 002
002
002
Tag






Valid
Address | Code
0003h | L1 LDH
... | 
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 30: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD
SUB
B
Cache
000
000
000
000 002
002
002
Tag






Valid
Address | Code
0003h | L1 LDH
... | 
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: Finally, we’re repeating our loops, therefore, we find our code on-chip. This is called a “cache hit”.
Yippee!

## Slide 31: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD
SUB
B
Cache
000
000
000
000 002
002
002
Tag






Valid
Address | Code
0003h | L1 LDH
... | 
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 32: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD
SUB
B
Cache
000
000
000
000 002
002
002
Tag






Valid
Address | Code
0003h | L1 LDH
... | 
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: This process continues.

## Slide 33: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B ADD B
SUB
B
Cache
000
000
000
000 002 000
002
002
Tag






Valid
Address | Code
0003h | L1 LDH
... | 
0026h | L2 ADD
0027h | SUB cnt
0028h | [!cnt] B L1
Notes: It looks like we got unlucky with one of our indexes. It keeps “thrashing”; that is, it get overwritten again and again by each routine. The 2K cache size keeps the thrashing minimized in the real world, but we wanted to show you what would happen.

## Slide 34: Direct-Mapped Cache Example
Index
0
1
2
3
4
5
6
7
8
9
A
.
.
F
LDH
MPY
ADD
B
ADD
SUB
B
Cache
000
000
000
000
002
002
002
Tag







Valid
Notes:
This example was contrived to show how cache lines can thrash
Code thrashing is minimized on the C6000 due to relatively large cache sizes
Keeping code in contiguous sections also helps to minimize thrashing
Let’s review the two types of misses that we encountered
Notes: It looks like we got unlucky with one of our indexes. It keeps “thrashing”; that is, it get overwritten again and again by each routine. The 2K cache size keeps the thrashing minimized in the real world, but we wanted to show you what would happen.

## Slide 35: Types of Misses
Compulsory
  Miss when first accessing an new address
Conflict
  Line is evicted upon access of an address whose index is already cached
  Solutions:
    Change memory layout
    Allow more lines for each index
Capacity (we didn’t see this in our example)
  Line is evicted before it can be re-used because capacity of the cache is exhausted
  Solution: Increase cache size

## Slide 36: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 37: Internal Memory Hierarchy
Internal
RAM or Cache
(L2)
CPU
Program Cache
(L1P)
Data Cache
(L1D)
EMIF
L1
Level 2
Level 3
We often refer to a system’s memory in hierarchical levels
Higher levels (L1) are closer to the CPU
CPU always requests from highest level memory …
… If address isn’t present in L1, cache h/w gets it from lower level
Looking more closely at L1P …
L3

## Slide 38: L1P Cache
DDR2
CPU
Program Cache (L1P)
L2
EMIF
How big is the cache?
Zero-waitstate Program Memory
Direct-Mapped Cache
  Works exceptionally well for DSP code (which tends to have many loops)
  Can be placed to minimize thrashing
for( i = 0; i < 10; i++ ) {
sum += x[i] * y[i];
}

## Slide 39: L1P Size
Device | Scheme | Size | Linesize | 
C62x/C67x | Direct Mapped | 4K bytes | 64 bytes (16 instr) | 
C64x | Direct Mapped | 16K bytes | 32 bytes (8 instr) | 
C64x+ C674x C66x | Direct Mapped | 32K bytes | 32 bytes (8 instr) | 
What does Linesize mean?
All L1P memories provide zero waitstate access

## Slide 40: New Term: Linesize
0x8000
0x8010
0x8020
Block
 |  | Cache
 | 0 | 
 | . . . | 
 | 0xF | 
In our earlier cache example, the size was:
  Size: 16 bytes
  Linesize: 1 byte
  # Of indexes: 16
How else could it be configured?
DDR2

## Slide 41: New Term: Linesize
0x8000
0x8010
0x8020
Block
 | Index | Cache | 
 | 0 | 0 | 1
 | . . . |  | 
 | 0x7 | 0xE | 0xF
In our earlier cache example, the size was:
  Size: 16 bytes
  Linesize: 1 byte
  # Of indexes: 16
If line size increases to TWO bytes, then:
  Size: 16 bytes
  Linesize: 2 bytes
  # Of indexes: 8
What’s the advantage of greater line size?
Speed! When cache retrieves one item, it gets another at the same time.
New C64x+ L1P features...
DDR2

## Slide 42: L1P Cache Comparison
Device | Scheme | Size | Linesize | New Features
C62x/C67x | Direct Mapped | 4K bytes | 64 bytes (16 instr) | N/A
C64x | Direct Mapped | 16K bytes | 32 bytes (8 instr) | N/A
C64x+ C674x C66x | Direct Mapped | 32K bytes | 32 bytes (8 instr) | Cache/RAM Cache Freeze Memory Protection
Next two slides discuss Cache/RAM and Freeze features. Memory Protection is not discussed in this workshop.
All L1P memories provide zero waitstate access
Cache/Ram...

## Slide 43: C64x+ L1P – Cache vs. Addressable RAM
32K |  |  |  |  |  |  |  |  | 
16K |  |  |  |  |  |  |  |  | 
8K |  |  |  |  |  |  |  |  | 
4K |  |  |  |  |  |  |  |  | 
Can be configured as Cache or Addressable RAM
Five cache sizes are available: 0K, 4K, 8K, 16K, 32K
Allows critical loops to be put into L1P, while still affording room for cache memory
 | RAM Memory
 | Cache
Cache Freeze...

## Slide 44: Cache Freeze (C64x+)
Freezing cache prevents data that is currently cached from being evicted
Cache Freeze
  Responds to read and write hits normally
  No updating of cache on miss
  Freeze supported on C64x+ L2/L1P/L1D
Commonly used with Interrupt Service Routines so that one-use code does not replace realtime algo code
Other cache modes: Normal, Bypass
Cache_xyz: BIOS Cache management module
Cache Mode Management
Mode = Cache_getMode(level) rtn state of specified cache
oldMode = Cache_setMode(level, mode) set state of specified cache
typedef enum {
CACHE_NORMAL, CACHE_FREEZE, CACHE_BYPASS
} CACHE_Mode;
typedef enum {
CACHE_L1D, CACHE_L1P, CACHE_L2
} CACHE_Level;

## Slide 45: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 46: Caching Data
for( i = 0; i < 4; i++ ) {
sum += x[i] * y[i];
}
One instruction may access multiple data elements:
Tag |  | Data Cache
 | 0 | 
 | 32K | 
What would happen if x and y ended up at the following addresses?
  x = 0x0000
  y = 0x8000
DDR2
x
y
They would end up overwriting each other in the cache --- called thrashing
Increasing the associativity of the cache will reduce this problem
How do you increase associativity?

## Slide 47: Increased Associativity
DDR2
0x00000
0x08000
0x10000
0x18000
 |  | Valid |  | Tag |  | Data Cache
 |  |  |  |  | 0 | 
 |  |  |  |  | 16K | 
 |  |  |  |  | 0 | 
 |  |  |  |  | 16K | 
Way 0
Way 1
Split a Direct-Mapped Cache in half
  Each half is called a cache way
  Multiple ways make data caches more efficient
What is a set?

## Slide 48: What is a Set?
0x8000
The lines from each way that map to the same index form a set
0x8008
0x8010
0x8018
 |  | Data Cache
 | 0 | 
 | 0 | 
Set of index zeroes,
i.e. Set 0
The number of lines per set defines the cache as an N-way set-associative cache
Set 1
Now, how many unique locations are there for each memory address?
DDR2

## Slide 49: What is a Set?
0x8000
The lines from each way that map to the same index form a set
0x8008
0x8010
0x8018
 |  | Data Cache
 | 0 | 
 | 0 | 
Set of index zeroes,
i.e. Set 0
The number of lines per set defines the cache as an N-way set-associative cache
With 2 ways, there are now 2 unique cache locations for each memory address
How do you determine WHICH line gets replaced? (LRU algo)
Set 1
L1D Summary...
DDR2

## Slide 50: L1D Summary
Device | Scheme | Size | Linesize | New Features
C62x/C67x | 2-Way Set Assoc. | 4K bytes | 32 bytes | N/A
C64x | 2-Way Set Assoc. | 16K bytes | 64 bytes | N/A
C64x+ C674x C66x | 2-Way Set Assoc. | C6455: 32K DM64xx: 80K | 64 bytes | Cache/RAM Cache Freeze Memory Protection
All L1D memories provide zero waitstate access
Cache/RAM configuration and Cache Freeze work similar to L1P
L1 caches are ‘Read Allocate’, thus only updated on memory read misses

## Slide 51: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 52: Internal Memory (L2)
CPU
L1 Program
(L1P)
L1 Data
(L1D)
L2
Program & Data
Device | Size | L2 Features
C671x | 64KB - 128K | Unified (code or data) Config as Cache or RAM None, or 1 to 4 way cache
C64x | 64KB - 1MB | Unified (code or data) Config as Cache or RAM Cache is always 4-way
C64x+ | 64KB - 2MB | Unified (code or data) Config as Cache or RAM Cache is always 4-way Cache Freeze Memory Protection
L2 linesize for all devices is 128 bytes
L2 caches are ‘Read/Write Allocate’ memories
L2 Cache Configuration...
Notes: The CPU can access two dedicated level-1 caches. A 4K direct-mapped cache for program code and a 2-way data cache. These level-1 caches provide single-cycle access to the CPU.
The level-2 memory is larger and a bit slower. It’s accessed whenever there is a level-1 cache miss. Even though it’s a little slower than the level-1 memory, it’s still faster than going off-chip. If the term “level-2 cache” sounds familiar, it’s because many personal computers now employ this same type of mechanism.
The level-1 vs. level-2 access is all automatic. YOU, the programmer, don’t have to worry about a thing. Just write your code as you’d normally would and the hardware figures out the quickest way to get the CPU your code and data.
What if the code/data isn’t in either the level-1 or level-2 memory? Then ...

## Slide 53: C64x+/C674x – L2 Memory Configuration
Configuration
  2MB on C6455
  When enabled, it’s always 4-Way (same as C64x)
Linesize
  Linesize = 128 bytes
  Same linesize as C671x & C64x
Performance
  L2  L1P
    1-8 Cycles
  L2  L1D
    L2 SRAM hit: 12.5 cycles
    L2 Cache hit: 14.5 cycles
    Pipelined: 4 cycles
    When required, minimize latency by using L1D RAM
L2 Ways are Configurable in Size
0
32K
64K
128K
256K
Using the Config Tool...

## Slide 54: Configuring L1/L2 Cache with the Config Tool
Use the Platform Package to specify the sizes of L1, L2 caches:
The default settings are:
L1D: 32K
L1P: 32K
L2: 0K

## Slide 55: Cache Performance Summary
Device | L1P | L1D | L2 Performance
C62x/C67x | Zero Waitstate Cache | Zero Waitstate Cache | L2 → L1P: 16 instr in 5 cycles L2 → L1D: 32 bytes in 4 cycles
C64x | Zero Waitstate Cache | Zero Waitstate Cache | L2 → L1P: 8 instr in 1-8 cycles L2 → L1D: 64 bytes in: L2 SRAM: 6 cycles L2 Cache: 8 cycles Pipelined: 2 cycles
C64x+ C674x C66x | Zero Waitstate Cache/RAM | Zero Waitstate Cache/RAM | L2 → L1P: 8 instr in 1-8 cycles L2 → L1D: 64 bytes in: L2 SRAM: 12.5 cycles L2 Cache: 14.5 cycles Pipelined: 4 cycles

## Slide 56: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 57: Coherency Example: Description
CPU
L2
DDR2
L1D
For this example, L2 is set up as cache
Example’s Data Flow:
  EDMA fills RcvBuf in DDR
  CPU reads RcvBuf, processes data, and writes to XmtBuf
  EDMA moves data from XmtBuf (e.g. to a serial port xmt)
RcvBuf
XmtBuf
EDMA
EDMA
Cache

## Slide 58: EDMA Writes Buffer - RCV
CPU
L2
L1D
RcvBuf
EDMA
Buffer (in external memory) written by the EDMA
DDR2

## Slide 59: CPU Reading Buffers - RCV
CPU
L2
L1D
RcvBuf
EDMA
CPU reads the buffer for processing
This read causes a cache miss in L1D and L2
DDR2

## Slide 60: CPU Reading Buffers - RCV
CPU
L2
L1D
RcvBuf
RcvBuf
RcvBuf
EDMA
CPU reads the buffer for processing
This read causes a cache miss in L1D and L2
The RcvBuf is added to both caches
  Space is allocated in each cache
  L2 is R/W allocate, L1 is read-allocate only
DDR2
What happens on the WRITE?

## Slide 61: Where Does the CPU Write To?
CPU
L2
L1D
RcvBuf
XmtBuf
After processing, the CPU writes to XmtBuf
Write misses to L1D are written directly to the next level of memory (L2)
Thus, the write does not go directly to external memory
Cache line Allocated: L1D on Read only L2 on Read or Write
XmtBuf
EDMA
DDR2

## Slide 62: Coherency Issue – Write
CPU
L2
L1D
XmtBuf
RcvBuf
EDMA
EDMA is set up to transfer the buffer from ext. mem
The buffer resides in cache, not in ext. memory
So, the EDMA transfers whatever is in ext. memory, probably not what you wanted
What is the solution?
XmtBuf
DDR2

## Slide 63: Coherency Solution – Write (Flush/Writeback)
CPU
L2
L1D
XmtBuf
RcvBuf
XmtBuf
EDMA
When the CPU is finished with the data (and has written it to XmtBuf in L2), it can be sent to ext. memory with a cache writeback
A writeback is a copy operation from cache to memory, writing back the modified (i.e. dirty) memory locations – all writebacks operate on full cache lines
Use BIOS Cache APIs to force a writeback:
writeback
BIOS: Cache_wb (XmtBuf, BUFFSIZE, CACHE_NOWAIT);
DDR2
What happens with the "next" RCV buffer?

## Slide 64: Coherency Issue – Read
CPU
L2
L1D
RcvBuf
RcvBuf
RcvBuf
EDMA
EDMA writes a new RcvBuf buffer to ext. memory
When the CPU reads RcvBuf a cache hit occurs since the buffer (with old “stale” data) is still valid in cache
Thus, the CPU reads the old data instead of the new
DDR2
Solution?

## Slide 65: Coherency Solution – Read
CPU
L2
L1D
RcvBuf
RcvBuf
RcvBuf
EDMA
To get the new data, you must first invalidate the old data before trying to read the new data (clears cache line’s valid bits)
Again, cache operations (writeback, invalidate) operate on cache lines
BIOS provides an invalidate option:
BIOS: Cache_inv (RcvBuf, BUFFSIZE, CACHE_WAIT);
DDR2

## Slide 66: BIOS Cache Functions Summary
blockPtr : start address of range to be invalidated
byteCnt : number of bytes to be invalidated
Wait : 1 = wait until operation is completed
Cache Invalidate | Cache_inv( blockPtr, byteCnt, wait )
 | Cache_invL1pAll()
Cache Writeback | Cache_wb( blockPtr, byteCnt, wait )
 | Cache_wbAll()
Invalidate & Writeback | Cache_wbInv( blockPtr, byteCnt, wait )
 | Cache_wbInvAll()
Sync waiting for Cache | Cache_wait()
What if the EDMA is reading/writing INTERNAL memory (L2)?

## Slide 67: Another Solution: Place Buffers in L2
CPU
L2
L1D
RcvBuf
RcvBuf
XmtBuf
EDMA
Configure some of L2 as RAM
Locate buffers in this RAM space
Coherency issues do not exist between L1D and L2
EDMA
To summarize Cache Coherency...
DDR2

## Slide 68: Coherence Summary
Internal (L1/L2) Cache Coherency is Maintained
Coherence between L1D and L2 is maintained by cache controller
No Cache_fxn operations needed for data stored in L1D or L2 RAM
L2 coherence operations implicitly operate upon L1, as well
Simple Rules for Error Free Cache (for DDR, L3)
TAKING OWNERSHIP – Before the DSP begins reading a shared external INPUT buffer, it should first BLOCK INVALIDATE the buffer
GIVING OWNERSHIP – After the DSP finishes writing to a shared external OUTPUT buffer, it should initiate an L2 BLOCK WRITEBACK
What about "cache alignment" ?
DEBUG NOTE: An easy way identify cache coherency problems is to allocate your buffers in L2. Problem goes away? It’s probably a cache coherency issue.

## Slide 69: Cache Alignment
False Addresses
False Addresses
Buffer
Buffer
Buffer
Cache Lines
Problem: How can I invalidate (or writeback) just the buffer?
In this case, you can’t
Definition: False Addresses are ‘neighbor’ data in the cache line, but outside the buffer range
Why Bad: Writing data to buffer marks the line ‘dirty’, which will cause entire line to be written to external memory, thus
External neighbor memory could be overwritten with old data
Avoid “False Address” problems by aligning buffers to cache lines (and filling entire line)
  Align memory to 128 byte boundaries
  Allocate memory in multiples of 128 bytes
#define BUF 128
#pragma DATA_ALIGN (in, BUF)
short in[256];

## Slide 70: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 71: "Turn Off" the DATA Cache (MAR)
CPU
L2
L1D
RcvBuf
XmtBuf
EDMA
Memory Attribute Registers (MARs) enable/disable DATA caching memory ranges
Don’t use MAR to solve basic cache coherency – performance will be too slow
Use MAR when you have to always read the latest value of a memory location, such as a status register in an FPGA, or switches on a board.
MAR is like “volatile”. You must use both to always read a memory location: MAR for cache; volatile for the compiler
Looking more closely at the MAR registers ...
DDR2

## Slide 72: Memory Attribute Regs (MAR) – DATA
CS2
CS4
CS5
0 = Not cached
1 = Cached
MAR4 0
MAR5 1
MAR6 1
MAR7 1
Reserved
Use MAR registers to enable/disable caching of external DATA ranges
Useful when external data is modified outside the scope of the CPU
You can specify MAR values in Config Tool
C671x:
  16 MARs
  4 per CE space
  Each handles 16MB
C64x/C64x+/C674x:
  Each handles 16MB
  256/224 MARs
  16 per CS space (on current C64x, some are rsvd)
Setting MARs in CFG files ...
Notes: (MAR is to CPU/Cache as volatile is to compiler)

## Slide 73: Memory Attribute Registers : MARs
Start Address | End Address | Size | Space
0x6000 0000 | 0x60FF FFFF | 16MB | CS2_
0x6200 0000 | 0x62FF FFFF | 16MB | CS3_
0x6400 0000 | 0x64FF FFFF | 16MB | CS4_
0x6600 0000 | 0x66FF FFFF | 16MB | CS5_
0xC000 0000 | 0xDFFF FFFF | 512MB | DDR2
MAR | MAR Address | EMIF Address Range
192 | 0x0184 8200 | C000 0000 – C0FF FFFF
193 | 0x0184 8204 | C100 0000 – C1FF FFFF
194 | 0x0184 8208 | C200 0000 – C2FF FFFF
195 | 0x0184 820C | C300 0000 – C3FF FFFF
196 | 0x0184 8210 | C400 0000 – C4FF FFFF
197 | 0x0184 8214 | C500 0000 – C5FF FFFF
... |  | 
223 |  | DF00 0000 – DFFF FFFF
256 MAR bits define cache-ability of 4G of addresses as 16MB groups
Many 16MB areas not used or present on given board
Example: Usable 6748 EMIF addresses at right
EVM6748 memory is:
  128MB of DDR2 starting at 0xC000 0000
  FLASH, NAND Flash, or SRAM in CS2_ space at 0x6000 0000
Note: with the C64x+ program memory is always cached regardless of MAR settings

## Slide 74: Configure MAR via GCONF (C6748)
First, add this line of script code to your .cfg file:
Then, modify the MAR settings:
Example: C6748 EVM
MAR 192-223 (DDR2) turned ‘on’
(starting at address 0xC000_0000)
OR Click

## Slide 75: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 76: L1D: DATA_MEM_BANK Example
Only one L1D access per bank per cycle
Use DATA_MEM_BANK pragma to begin paired arrays in different banks
Note: sequential data are not down a bank, instead they are along a horizontal line across banks, then onto the next horizontal line
Only even banks (0, 2, 4, 6) can be specified
512x32
0
1
2
3
20
21
22
23
512x32
4
5
6
7
24
25
26
27
512x32
8
9
A
B
28
29
2A
2B
512x32
C
D
E
F
2C
2D
2E
2F
512x32
10
11
12
13
30
31
32
33
512x32
14
15
16
17
34
35
36
37
512x32
18
19
1A
1B
38
39
3A
3B
512x32
1C
1D
1E
1F
3C
3D
3E
3F
Bank 0
Bank 2
Bank 4
Bank 6
#pragma DATA_MEM_BANK(a, 4); short a[256];
#pragma DATA_MEM_BANK(x, 0); short x[256];
for(i = 0; i < count ; i++) sum += a[i] * x[i];
Optimizing the cache...

## Slide 77: Cache Optimization
Optimize for Level 1
Multiple Ways and wider lines maximize efficiency –
  TI did this for you!
Main Goal - maximize line reuse before eviction
  Algorithms can be optimized for cache
“Touch Loops” can help with compulsory misses
  Run once thru loop in init code
  Touch buffers to “pre-load” data cache
Up to 4 write misses can happen sequentially, but the next read or write will stall
  Bus has 4 deep buffer between CPU/L1 and beyond
Be smart about data output by one function then read by another (touch it first)
  When data is output by first function, where does it go?
  If you touch output buffer first, then where will output data go?
Docs...

## Slide 78: Updated Cache Documentation
Cache Reference
  More comprehensive description of C6000 cache
  Revised terminology for cache coherence operations
Cache User’s Guide
  Cache Basics
  Using C6000 Cache
  Optimization for Cache Performance
SPRU656: C62x/C64x/C67
SPRU862: C64x+/C674
SPRUGY8: C66x
SPRU609: C621x/C671x
SPRU610: C64x
SPRU871: C64x+/C674
SPRUGW0: C66x
Summary...

## Slide 79: Cache Aware Linking
Procedure
Profile code for L1P cache misses - don’t solve a problem that doesn’t exist
Instrument your app by building with compiler option (--gen_profile_info)
Run instrumented app to generate profile data (.ppd)
Decode profile data file (.prf)
Generate WCG data (.csv) for each source file
Generate linker command file (.cmd file)
Re-build of the app with optimized function ordering
Goal
Re-arrange functions to reduce L1P conflict misses
How it works
CGT v7.0 contains a new cache layout tool (clt6x). It takes dynamic profile info to create a preferred function ordering linker command file that guides the placement of function subsections
More Info
http://processors.wiki.ti.com/index.php/Program_Cache_Layout

## Slide 80: Cache – General Terminology
Associativity: The # of places a piece of data can map to inside the cache.
Coherence: assuring that the most recent data gets written back from a cache when there is different data in the levels of memory
“Dirty”: When an allocated cache line gets changed/updated by the CPU (*file)
Read-allocate cache: only allocates space in the cache during a read miss. C64x+ L1 cache is read-allocate only.
Write-allocate cache: only allocates space in the cache during a write miss.
Read-write-allocate cache: allocates space in the cache for a read miss or a write miss. C64x+ L2 cache is read-write allocate.
Write-through cache: updates to cache lines will go to ALL levels of memory such that a line is never “dirty” (less efficient than WB cache – more DDR xfrs).
Write-back cache: updates occur only in the cache. The line is marked as “dirty” and if it is evicted, updates are pushed out to lower levels of memory. All C64x+ cache is write-back*.
Notes: True, C64x+ cache is write-back – but, the L1D will not cache writes unless the buffer is already present – per the “Read-allocate” rule.

## Slide 81: Outline
Why Cache?
Cache Basics
Cache Example
L1 Program
L1 Data
L2 Memory
Cache Coherency
MAR Registers
Add’l Topics
Quiz + Lab

## Slide 82: Chapter Quiz
How do you turn ON the cache ?
Name the three types of caches & their associated memories:
All cache operations affect an aligned cache line. How big is a line?
Which bit(s) turn on/off “cacheability” and where do you set these?
How do you fix coherency when two bus masters access ext’l mem?
If a dirty (newly written) cache line needs to be evicted, how does that dirty line get written out to external memory?

## Slide 83: Chapter Quiz
How do you turn ON the cache ?
Name the three types of caches & their associated memories:
All cache operations affect an aligned cache line. How big is a line?
Which bit(s) turn on/off “cacheability” and where do you set these?
How do you fix coherency when two bus masters access ext’l mem?
If a dirty (newly written) cache line needs to be evicted, how does that dirty line get written out to external memory?
Set size > 0 in platform package (or via Cache_setSize() during runtime)
Direct Mapped (L1P), 2-way (L1D), 4-way (L2)
L1P – 32 bytes (256 bits), L1D – 64 bytes, L2 – 128 bytes
Invalidate before a read, writeback after a write (or use L2 mem)
MAR (Mem Attribute Register), affects 16MB Ext’l data space, .cfg
Cache controller takes care of this

## Slide 84: Lab 14 – Using Cache
In this lab, we’ll benchmark different systems to compare results of turning the cache ON vs. OFF
This project is the SOLUTION from the previous lab (OPT)
We will take the OPT lab and apply different system settings as noted below:
Buffers in L2 – L1 Cache ON (default)
Everything Ext’l – Cache OFF (not real time)
Everything Ext’l – Cache ON (typical system)
Time: 30 Min
Note: this lab uses NEW i2c code for LED_toggle() – 4 new files (i2c/led)

## Slide 86: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal