## Slide 2: Objectives
Describe the basic architecture of the C66x family of devices
Provide an overview of each device subsystem
Describe the basic features of the Multicore Software Development Kit (MCSDK)

## Slide 3: Outline
C66x Family Overview
C6000 Roadmap
C667x Architecture Overview
C665x Low-Power Devices
MCSDK Overview

## Slide 4: Outline
C66x Family Overview
C6000 Roadmap
C667x Architecture Overview
C665x Low-Power Devices
MCSDK Overview

## Slide 5: Enhanced DSP core
100% upward object code compatible
4x performance improvement for multiply operation
32 16-bit MACs
Improved support for complex arithmetic and matrix computation
IEEE 754 Native Instructions for SP & DP
Advanced VLIW architecture
2x registers
Enhanced floating-point add capabilities
100% upward object code compatible with C64x, C64x+, C67x and c67x+
Best of fixed-point and floating-point architecture for better system performance and faster time-to-market.
Advanced fixed-point instructions
Four 16-bit or eight 8-bit MACs
Two-level cache
SPLOOP and 16-bit instructions for smaller code size
Flexible level one memory architecture
iDMA for rapid data transfers between local memories
C66x ISA
C64x+
C64x
C67x
C67x+
FLOATING-POINT VALUE
FIXED-POINT VALUE
Performance improvement
C674x
Notes: 5

## Slide 6: Outline
C66x Family Overview
C6000 Roadmap
C667x Architecture Overview
C665x Low-Power Devices
MCSDK Overview

## Slide 7: CorePac
1 to 8 C66x CorePac DSP Cores operating at up to 1.25 GHz
  Fixed/Floating-pt operations
  Code compatible with other C64x+ and C67x+ devices
L1 Memory
  Partition as Cache or RAM
  32KB L1P/D per core
Dedicated L2 Memory
  Partition as Cache or RAM
  512 KB to 1 MB per core
Direct connection to memory subsystem
CorePac
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
64-bit
DDR3 EMIF
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
HyperLink
TeraNet
Common and App-specific I/O
L1D
L2
Network Coprocessor

## Slide 8: Memory Subsystem
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
HyperLink
TeraNet
L1D
L2
Memory Subsystem
64-bit
DDR3 EMIF
Multicore Shared Memory (MSM SRAM)
  2 to 4MB (Program or Data)
  Available to all cores
Multicore Shared Mem (MSMC)
  Arbitrates access to shared memory and DDR3 EMIF
  Provides CorePac access to coprocessors and I//O
  Provides address extension to 64G (36 bits)
DDR3 External Memory Interface (EMIF) – 8GB
  Support for 16/32/64-bit modes
  Specified at up to 1600 MT/s
Network Coprocessor
Common and App-specific I/O
CorePac

## Slide 9: Multicore Navigator
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Packet DMA
Multicore Navigator
Queue Manager
Network Coprocessor
C66x™
CorePac
L1P
HyperLink
TeraNet
L1D
L2
Memory Subsystem
CorePac
64-bit
DDR3 EMIF
Provides seamless inter-core communications (msgs and data) between cores, IP, and peripherals. “Fire and forget”
Low-overhead processing and routing of packet traffic to/from cores and I/O
Supports dynamic load optimization
Consists of a Queue Manager Subsystem (QMSS) and multiple, dedicated Packet DMA engines
Multicore Navigator
Common and App-specific I/O

## Slide 10: Multicore Navigator Architecture

## Slide 11: Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
HyperLink
TeraNet
L1D
L2
Memory Subsystem
CorePac
64-bit
DDR3 EMIF
Multicore Navigator
Network Coprocessor
Provides H/W accelerators to perform L2, L3, L4 processing and encryption (often done in S/W)
Packet Accelerator (PA)
  8K multi-in/out HW queues
  Single IP address option
  UDP/TCP checksum and CRCs
  Quality of Service (QoS) support
  Multi-cast to multiple queues
Security Accelerator (SA)
  HW encryption, decryption and authentication
  Supports protocols: IPsec ESP, IPsec AH, SRTP, 3GPP
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
PA
SA
Common and App-specific I/O
Network Coprocessor

## Slide 12: External Interfaces
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
HyperLink
TeraNet
L1D
L2
Memory Subsystem
CorePac
64-bit
DDR3 EMIF
Multicore Navigator
Network Coprocessor
2x SGMII ports – support 10/100/1000 Ethernet
4x SRIO lanes for inter-DSP xfrs
SPI for boot operations
UART for development/test
2x PCIe at 5Gbps
I2C for EPROM at 400 Kbps
GPIO
App-specific interfaces
Network Coprocessor
External Interfaces
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
Application
Specific I/O
Application
Specific I/O
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Common and App-specific I/O

## Slide 13: TeraNet Switch Fabric
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
HyperLink
TeraNet
L1D
L2
64-bit
DDR3 EMIF
Non-blocking switch fabric that enables fast and contention-free data movement
Can configure/manage traffic queues and priorities of xfrs while minimizing core involvement
High-bandwidth transfers between cores, subsystems, peripherals and memory
Network Coprocessor
Common and App-specific I/O
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor

## Slide 14: TeraNet Data Connections
QMSS
MSMC
DDR3
Shared L2
S
S
Core
S
PCIe
S
TAC_BE
S
SRIO
PCIe
QMSS
M
M
M
TPCC
16ch QDMA
M
TC0
M
TC1
M
M
DDR3
XMC
M
DebugSS
M
TPCC
64ch
QDMA
M
TC2
M
TC3
M
TC4
M
TC5
TPCC
64ch
QDMA
M
TC6
M
TC7
M
TC8
M
TC9
Network
Coprocessor
M
HyperLink
M
HyperLink
S
AIF / PktDMA
M
FFTC / PktDMA
M
RAC_BE0,1
M
TAC_FE
M
SRIO
S
S
RAC_FE
S
TCP3d
S
TCP3e_W/R
S
VCP2 (x4)
S
M
EDMA_0
EDMA_1,2
Core
S
M
Core
S
M
L2 0-3
S
M
Facilitates high-bandwidth communication links between DSP cores, subsystems, peripherals, and memories.
Supports parallel orthogonal communication links
CPUCLK/2
256bit TeraNet
FFTC / PktDMA
M
TCP3d
S
RAC_FE
S
VCP2 (x4)
S
VCP2 (x4)
S
VCP2 (x4)
S
RAC_BE0,1
M
CPUCLK/3
128bit TeraNet
S
S
S
S
Notes: CPT see physical addresses. In MSMC, one CPT per bank.

## Slide 15: Diagnostic Enhancements
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
HyperLink
TeraNet
L1D
L2
64-bit
DDR3 EMIF
Network Coprocessor
Common and App-specific I/O
Diagnostic Enhancements
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor
Embedded Trace Buffers (ETB) enhance CorePac’s diagnostic capabilities
CP Monitor provides diagnostics on TeraNet data traffic
Automatic statistics collection and exporting (non-intrusive)
Can monitor individual events
Monitor all memory transactions
Configure triggers to determine when data is collected
Debug & Trace

## Slide 16: HyperLink Bus
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
TeraNet
L1D
L2
64-bit
DDR3 EMIF
Network Coprocessor
Common and App-specific I/O
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor
Expands the TeraNet Bus to external devices
Supports 4 lanes with up to 12.5Gbaud per lane
HyperLink Bus
Diagnostic Enhancements
HyperLink

## Slide 17: Miscellaneous Elements
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
TeraNet
L1D
L2
64-bit
DDR3 EMIF
Network Coprocessor
Common and App-specific I/O
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor
Boot ROM
HW Semaphore provides atomic access to shared resources
Power Management
PLL1 (Corepacs), PLL2 (DDR3), PLL3 (Packet Acceleration)
Three EDMA Controllers
16 64-bit Timers
Inter-Processor Communication (IPC) Registers
Diagnostic Enhancements
HyperLink
Miscellaneous
HyperLink Bus
Power
Mgmt
Boot ROM
HW Sem
x3
PLL
EDMA
x3

## Slide 18: App-Specific: Wireless Applications
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
TeraNet
L1D
L2
64-bit
DDR3 EMIF
Network Coprocessor
Common and App-specific I/O
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor
Diagnostic Enhancements
HyperLink
FFTC
TCP3d
TCP3e
x2
x2
Coprocessors
VCP2
x4
BCP
Wireless Applications
Miscellaneous
HyperLink Bus
Application-Specific
Wireless-specific Coprocessors
  2x FFT Coprocessor (FFTC)
  Turbo Dec/Enc (TCP3D/3E)
  4x Viterbi Coprocessor (VCP2)
  Bit-rate Coprocessor (BCP)
  2x Rake Search Accel (RSA)
Wireless-specific Interfaces
  6x Antenna Interface (AIF2)
AIF2 x6
RSA
C6670

## Slide 19: App-Specific: General Purpose
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM SRAM
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
C66x™
CorePac
L1P
TeraNet
L1D
L2
64-bit
DDR3 EMIF
Network Coprocessor
Common and App-specific I/O
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor
Diagnostic Enhancements
HyperLink
EMIF 16
TSIP x2
General Purpose Applications
Miscellaneous
HyperLink Bus
Wireless Applications
2x Telecom Serial Port (TSIP)
EMIF 16 (EMIF-A):
  Connects memory up to 256MB
  Three modes:
    Synchronized SRAM
    NAND Flash
    NOR Flash

## Slide 20: Keystone Device Architecture
TeraNet Switch Fabric
Memory Subsystem
Multicore Navigator
CorePac
External Interfaces
Network Coprocessor
Diagnostic Enhancements
General Purpose Applications
Miscellaneous
HyperLink Bus
Wireless Applications
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
GPIO
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
HyperLink
TeraNet
Application
Specific I/O
Application
Specific I/O
MSMC
MSM SRAM
Memory Subsystem
64-bit
DDR3 EMIF
C66x™
CorePac
L1P
L1D
L2
1 to 8 Cores @ up to 1.25 GHz

## Slide 21: Outline
C66x Family Overview
C6000 Roadmap
C667x Architecture Overview
C665x Low-Power Devices
MCSDK Overview

## Slide 22: Keystone C6655/57 – Device Features
C6655/57 Low-Power Devices
1 or 2 Cores @ up to 1.25 GHz
C66x™
CorePac
VCP2
C6655/57
MSMC
1MB
MSM
SRAM
32-Bit
DDR3 EMIF
TCP3d
x2
Coprocessors
Memory Subsystem
Packet
DMA
Multicore Navigator
Queue
Manager
x2
32KB L1
P-Cache
32KB L1
D-Cache
1024KB L2 Cache
PLL
EDMA
HyperLink
TeraNet
Ethernet
MAC
SGMII
S
R
I
O
x4
S
P
I
U
A
R
T
x2
P
C
I
e
x2
I2C
U
P
P
M
c
B
S
P
x2
G
P
I
O
E
M
I
F
1
6
Boot ROM
Debug & Trace
Power
Management
Semaphore
Security /
Key Manager
Timers
2nd core, C6657 only
C66x CorePac
  C6655 (1 core) @ 1/1.25 GHz
  C6657 (2 cores) @ 0.85, 1.0 or 1.25 GHz
Memory Subsystem
  1MB Local L2 per core
  MSMC , 32-bit DDR3 I/F
Hardware Coprocessors
  TCP3d, VCP2
Multicore Navigator
Interfaces
  2x McBSP, SPI, I2C, UPP, UART
  1x 10/100/1000 SGMII port
  Hyperlink, 4x SRIO, 2x PCIe
  EMIF 16, GPIO
Debug and Trace (ETB/STB)

## Slide 23: Keystone C6654 – Power Optimized
C6654 – Power Optimized
1 Core @ 850 MHz
C66x™
CorePac
C6654
MSMC
32-Bit
DDR3 EMIF
Memory Subsystem
Packet
DMA
Multicore Navigator
Queue
Manager
x2
32KB L1
P-Cache
32KB L1
D-Cache
1024KB L2 Cache
PLL
EDMA
TeraNet
Ethernet
MAC
SGMII
S
P
I
U
A
R
T
x2
P
C
I
e
x2
I2C
U
P
P
M
c
B
S
P
x2
G
P
I
O
E
M
I
F
1
6
Boot ROM
Debug & Trace
Power
Management
Semaphore
Security /
Key Manager
Timers
C66x CorePac
  C6654 (1 core) @ 850 MHz
Memory Subsystem
  1MB Local L2
  MSMC , 32-bit DDR3 I/F
Multicore Navigator
Interfaces
  2x McBSP, SPI, I2C, UPP, UART
  1x 10/100/1000 SGMII port
  EMIF 16, GPIO
Debug and Trace (ETB/STB)

## Slide 24: Keystone C665x – Comparisons
HW Feature | C6654 | C6655 | C6657
CorePac Frequency (GHz) | 0.85 | 1 @ 1.0, 1.25 | 2 @ 0.85, 1.0, 1.25
Multicore Shared Mem (MSM) | No | 1MB SRAM | 
DDR3 Maximum Data Rate | 1066 | 1333 | 
Serial Rapid I/O (SRIO) Lanes | No | 4x | 
HyperLink | No | Yes | 
Viterbi CoProcessor (VCP) | No | 2x | 
Turbo Decoder (TCP3d) | No | Yes | 

## Slide 25: For More Information
For more information, refer to the C66x Getting Started page to locate the data manual for your KeyStone device.
View the complete C66x Multicore SOC Online Training for KeyStone Devices, including details on the individual modules.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.
Notes: NEW

## Slide 26: Outline
C66x Family Overview
MCSDK Overview
What is the MCSDK ?
Software Architecture
For More Info…

## Slide 27: Outline
C66x Family Overview
MCSDK Overview
What is the MCSDK ?
Software Architecture
For More Info…

## Slide 28: What is MCSDK?
The Multicore Software Development Kit (MCSDK) provides the core foundational building blocks for customers to quickly start developing embedded applications on TI high performance multicore DSPs.
  Uses the SYS/BIOS or Linux real-time operating system
  Accelerates customer time to market by focusing on ease of use and performance
  Provides multicore programming methodologies
Available for free on the TI website bundled in one installer, all the software in the MCSDK is in source form along with pre-built libraries

## Slide 29: Software Development Ecosystem Multicore Performance, Single-core Simplicity
Editor
CodeGen
OpenMP
Profiler
Debugger
Remote
Debug
Multicore System
Analyzer
Visualization
Host Computer
Target Board
Eclipse
PolyCore
ENEA
Optima
3L
Critical
Blue
Multicore Software Development Kit
Code
Composer
StudioTM
Third
Party
Plug-Ins
XDS 560 V2
XDS 560 Trace

## Slide 30: MCSDK Variants
Name | Release | DSP | ARM | OS | Notes
BIOS-MCSDK | 1.x, 2.x | x | NA | SYS/BIOS | DSP-only SOC running SYS/BIOS real-time operating system
Linux-MCSDK | 1.x, 2.x | x | NA | Linux on DSP | DSP-only SOC running Linux real-time operating system

## Slide 31: Outline
C66x Family Overview
MCSDK Overview
What is the MCSDK ?
Software Architecture
For More Info…

## Slide 32: Migrating Development Platform
May be used “as is” or customer can implement value-add modifications
Needs to be modified or replaced with customer version
No modifications required
CSL
TI Platform
Network
Dev Kit
Demo Application
TI Demo Application on TI Evaluation Platform
IPC
LLD
EDMA, Etc
Tools
(UIA)
CSL
Customer Platform
TI Demo Application on Customer Platform
IPC
LLD
Network
Dev Kit
EDMA, Etc
Tools
(UIA)
Demo Application
CSL
Customer Platform
Network
Dev Kit
IPC
LLD
EDMA, Etc
Tools
(UIA)
Customer Application on Customer Platform
Customer Application
CSL
Next Gen TI Platform
Network
Dev Kit
IPC
LLD
EDMA, Etc
Tools
(UIA)
Customer App on Next Generation TI SOC Platform
Customer Application
Software may be different, but API remain the same (CSL, LLD, etc.)

## Slide 33: BIOS-MCSDK Software
Hardware
SYS/BIOS
RTOS
Software Framework Components
Interprocessor
Communication
Instrumentation
(MCSA)
Communication Protocols
TCP/IP
Networking
(NDK)
Algorithm Libraries
DSPLIB
IMGLIB
MATHLIB
Demonstration Applications
HUA/OOB
IO Bmarks
Image
Processing
Low-Level Drivers (LLDs)
Chip Support Library (CSL)
EDMA3
PCIe
PA
QMSS
SRIO
CPPI
FFTC
HyperLink
TSIP
…
Platform/EVM Software
Bootloader
Platform
Library
POST
OSAL
Resource
Manager
Transports - IPC - NDK

## Slide 34: Interprocessor Communication (IPC)
Device 1
SoC Hardware and Peripherals
Core 1
IPC
Process 1
Process 2
BIOS
Core 2
IPC
Process 1
Process 2
BIOS
Device 2
SoC Hardware and Peripherals
Core 1
IPC
Process 1
Process 2
BIOS
Core 2
IPC
Process 1
Process 2
BIOS
Device 1
SoC Hardware and Peripherals
Core 1
SysLink
Process 1
Process 2
Linux
Core 2
IPC
Process 1
Process 2
BIOS
Core 3
IPC
Process 1
Process 2
BIOS
Core N
IPC
Process 1
Process 2
BIOS
IPC Transports | Task to Task | Core to Core | Device to Device
Shared Memory | x | x | 
Navigator/QMSS | x | x | 
SRIO | x | x | x
PCIe | x | x | x
HyperLink | x | x | x

## Slide 35: MessagQ – Message Queue
Example:
QUE
...
MessageQ_get(msg,q2);
…
…
…
…
…
…
…
…
MessageQ_put(q2,msg);
…
Thread 1
Thread 2
Blocked until flag (semaphore) posted (or timeout)
Wait for message to be posted
Post msg into queue
Post semaphore
Unblock blocked thread
+ any number of messages can be passed
+ message can be anything desired (beginning with MessageQ_header)
+ message notification is user specified (e.g. semaphore, polling, etc.)
+ API unchanged even when going trans-processor !
Notes: MSGQ_get cannot be done in an HWI. Instructor – going from SEM and QUE to MBX, then SCOM, then MSGQ is an evolutionary process. MBX, because it makes copies of the messages is slower and more cumbersome (but ok for short msgs – not that much overhead). For video systems, SCOM (an RF5 module) is preferred due to its higher performance and being able to pass ptrs to data buffers. MSGQ is the latest and “greatest” QUE/SEM API providing the user with lots of flexibility (esp the capability of talking between a DSP and GPP, e.g. OMAP). So, for many video systems, SCOM is the right choice. For others, that need the flexibility of MSGQ – then use it.

## Slide 36: MessageQ: Overview
Messaging protocol allows clients to send messages to a named Message Queue located on any processor in the system
Message Queue can have: single reader, multiple writers
Message Queue object
Reader
Writer 1
Writer n
So, the MessageQ object is associated with the READER…
Notes: Multiple writer, Single reader
MSGQ_get is blocking APIs – useful for synchronization
Check Programmer Guide -

## Slide 37: MessageQ Concepts (1/4)
READER
MessageQ
“myQ”
MsgQ transactions begin with listener opening a MsgQ (single reader, multi-talker)
Listener’s attempt to get a message results in a block (when semaphore specified), since no messages are in the queue yet
MsgQ_create( “myQ”, &hQ, ... );
MsgQ_get( hQ, &msg, ... );

## Slide 38: MessageQ Concepts (2/4)
MsgQ_open(“myQ”, &hQ, .. );
MsgQ_alloc( poolid, &msg, .. );
msg->myMsg = …;
MsgQ_put( msg, hQ );
WRITER
POOL
MSGQ_Header
myMsg
MyMsgqMsg
MSGQ
“myQ”
Talker begins by locating the MsgQ opened by the listener
Talker gets a message block from a pool and fills it as desired
Talker puts the message into the MsgQ
MsgQ_create( “myQ”, &hQ, ... );
MsgQ_get( hQ, &msg, ... );
typedef struct MyMsgqMsg {
MsgQ_MsgHeader header;
...
} MyMsg;
READER

## Slide 39: MessageQ Concepts (3/4)
MsgQ_open(“myQ”, &hQ, .. );
MsgQ_alloc( poolid, &msg, .. );
msg->myMsg = …;
MsgQ_put( msg, hQ );
MsgQ_create( “myQ”, &hQ, ... );
MsgQ_get( hQ, &msg, ... );
eval( msg->myMsg );
MsgQ_free( msg );
POOL
MsgQ_Header
myMsg
MyMsgqMsg
MSGQ
“myQ”
Once talker puts message to MsgQ, listener is unblocked
Listener can now read/evaluate received message
Listener frees message back to pool
WRITER
READER

## Slide 40: MessageQ Concepts (4/4)
MsgQ_open(“myQ”, &hQ, .. );
MsgQ_alloc( poolid, &msg, .. );
msg->myMsg = …;
MsgQ_put( msg, hQ );
`
MsgQ_create( “myQ”, &hQ, ... );
MsgQ_get( hQ, &msg, ... );
eval( msg->myMsg );
MsgQ_free( msg );
POOL
MsgQ_Header
myMsg
MyMsgqMsg
MSGQ
“myQ”
The message object manages queuing of messages passed
An allocator mechanism is for getting buffers; standard = POOL
A transport mechanism can be specified for trans-processor MsgQ (transport = SRIO or DSPLNK)
MsgQ APIs
Transports
POOL0
POOLN
. . .
Msg Pool
Msg Pool
WRITER
READER

## Slide 41: Packaging (BIOS-MCSDK)

## Slide 42: Outline
C66x Family Overview
MCSDK Overview
What is the MCSDK ?
Software Architecture
For More Info…

## Slide 43
EVM Flash Contents
NAND
64 MB
NOR
16 MB
EEPROM
128 KB
POST
IBL
BIOS MCSDK
“Out of Box” Demo
Linux MCSDK
Demo
Linux/BIOS MCSDK C66x Lite EVM Details
DVD Contents
Factory default recovery
  EEPROM: POST, IBL
  NOR: BIOS MCSDK Demo
  NAND: Linux MCSDK Demo
  EEPROM/Flash writers
CCS 5.0
  IDE
  C667x EVM GEL/XML files
BIOS MCSDK 2.0
  Source/binary packages
Linux MCSDK 2.0
  Source/binary packages
Online Collateral
TMS320C667x processor website http://focus.ti.com/docs/prod/folders/print/tms320c6678.html http://focus.ti.com/docs/prod/folders/print/tms320c6670.html
MCSDK website for updates http://focus.ti.com/docs/toolsw/folders/print/bioslinuxmcsdk.html
CCS v5 http://processors.wiki.ti.com/index.php/Category:Code_Composer_Studio_v5
Developer’s website Linux: http://linux-c6x.org/
BIOS: http://processors.wiki.ti.com/index.php/BIOS_MCSDK_2.0_User_Guide
Notes: 43

## Slide 44: For More Information
For questions regarding topics covered in this training, visit the following e2e support forums:
http://e2e.ti.com/support/dsp/c6000_multi-core_dsps/f/639.aspx
Download MCSDK software:
http://focus.ti.com/docs/toolsw/folders/print/bioslinuxmcsdk.html
Refer to the MCSDK User’s Guide:
http://processors.wiki.ti.com/index.php/BIOS_MCSDK_2.0_User_Guide
http://e2e.ti.com/support/embedded/f/355.aspx
User’s Guide
Download Software
Software Forums

## Slide 46: TMS320C674x Architecture - Overview
128K L3
16-bit EMIF
DDR2 mDDR
McASP
MMC/SD
EMAC
HPI
SATA
I2C, SPI, UART
Switched Central Resource (SCR)
256K
L2
EDMA3
32KB L1P Cache/SRAM
32KB L1D Cache/SRAM
4-32x PLL
Performance & Memory
TMS320C6748
128
128
256
128
Communications
Up to 456MHz
256K L2 (cache/SRAM)
32K L1P/D Cache/SRAM
16-bit DDR2-266
16-bit EMIF (NAND Flash)
64-Channel EDMA 3.0
10/100 EMAC
USB 1.1 & 2.0
SATA
Power/Packaging
13x13mm nPBGA & 16x16mm PBGA
Pin-to-pin compatible w/OMAP L138 (+ARM9), 361-pin pkg
Dynamic voltage/freq scaling
Total Power < 420mW
128
128
USB
Timers
LCD, PWM, eCAP
uPP
Notes: mDDR – mobile DDR

## Slide 47: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal