## Slide 2: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 3: What is “DMA” ?
When we say “DMA”, what do we mean? Well, there are MANY forms of “DMA” (Direct Memory Access) on this device:
EDMA3 – “Enhanced” DMA handles 64 DMA CHs and 4 QDMA CHs
DMA – 64 channels that can be triggered manually or by events/chaining
QDMA – 8 channels of “Quick” DMA triggered by writing to a “trigger word”
IDMA – 2 CHs of “Internal” DMA (Periph Cfg, Xfr L1 ↔ L2)
Peripheral “DMA”s – Each master device hooked to the Switched Central Resource (SCR) has its own DMA (e.g. SRIO, EMAC, etc.)
Ch0
L1D
L2
PERIPH
Ch1
L1
L2
IDMA
Q0
Q1
Q2
Q3
TC0
TC1
TC2
TC3
SCR
QDMA
EVTx
Chain
Manual
EDMA3
DMA
Trigger Word
Switched Central Resource
64
4
Notes: It is important to point out the different definitions of “DMA” and when these items are covered in the workshop. Chapter 5 is primarily focussed on the 64-channel DMA as part of the EDMA3 module. Chapter 6 also covers details on EDMA3 and contains 3 slides on QDMA. Chapter 9 – Optimizations – will cover IDMA.

## Slide 4: Multiple DMA’s : EDMA3 and QDMA
VPSS
C64x+ DSP
L1P
L1D
L2
EDMA3
(System DMA)
DMA
(sync)
QDMA
(async)
DMA
Enhanced DMA (version 3)
DMA to/from peripherals
Can be sync’d to peripheral events
Handles up to 64 events
QDMA
Quick DMA
DMA between memory
Async – must be started by CPU
4-16 channels available
128-256 Parameter RAM sets (PARAMs)
64 transfer complete flags
2-4 Pending transfer queues
Both Share (number depends upon specific device)
Master Periph
Notes: DM6437 – 128 PSETS, 8 QDMA channels, 3 Queues, 64 TCCs
DM6446 – 128/8/2/64
6455 – 256/4/4/64

## Slide 5: Multiple DMA’s : Master Periphs & C64x+ IDMA
C64x+ DSP
L1P
L1D
L2
IDMA
EDMA3
(System DMA)
DMA
(sync)
QDMA
(async)
IDMA
Built into all C64x+ DSPs
Performs moves between internal memory blocks and/or config bus
Don’t confuse with iDMA API
VPSS
Master Periph’s
Front End (capture)
Back End (display)
USB  ATA
Ethernet
VLYNQ
Master Peripherals
VPSS (and other master periph’s) include their own DMA functionality
USB, ATA, Ethernet, VLYNQ share bus access to SCR
Notes:  Both ARM and DSP can access the EDMA3  Only DSP can access hardware IDMA

## Slide 6: SCR & EDMA3
EDMA3
TC0
TC1
TC2
EMAC HPI PCI
ARM
McASP
McBSP PCI
DDR2/3
L2 Mem Ctrl
L2
L1P
L1D
D
S
M
L
D
S
M
L
CPU
C64x+ MegaModule
M
S
S
M
M
S
IDMA
L1P Mem Ctrl
L1D Mem Ctrl
AET
DATA
SCR
CFG
SCR
EMIF
128
128
Cfg
PERIPH
M
S
M
S
Master
Slave
EDMA3 is a master on the DATA SCR – it can initiate data transfers
EDMA3’s configuration registers are accessed via the CFG SCR (by the CPU)
Each TC has its own connection (and priority) to the DATA SCR. Refer to the connection matrix to determine valid connections
32
PERIPH =
All peripheral’s
Cfg registers
SCR = Switched Central Resource
32
External Mem Cntl
CC x2
L3
Notes: This is somewhat of a simplification of the SCRs and megamodule diagrams in the datasheet.

## Slide 7: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 8: DMA : Direct Memory Access
Copy from memory to memory – HARDWARE memcpy(dst, src, len);
Faster than CPU LD/ST. One INT per block vs. one INT per sample
Import raw data from off-chip to on-chip before processing
Export results from on-chip to off-chip afterward
Transfer Configuration (i.e. Parameter Set - aka PaRAM or PSET)
Transfer configuration primarily includes 8 control registers
Goal :
Examples :
Controlled by :
Original
Data
Block
Copied
Data
Block
DMA
Transfer
Configuration
Source
ACNT
Destination
BCNT
Length
Notes: For ARM+DSP, resources are shared between ARM and DSP. ARM has some channels, DSP has other channels. If you’re using CE, this is taken care of for you. If you’re NOT using CE, it is up to you to manage resources.

## Slide 9: How Much to Move?
Element
(# of contig bytes)
A Count (Element Size)
0
15
Options
Source
Destination
Index
Link Addr
Cnt Reload
Transfer Count
“A” Count
16
31
B Count (# Elements)
Elem 1
Elem 2
Elem N
Frame
. .
“B” Count
Index
Index
C
Rsvd
Frame 1
Frame 2
Frame M
Block
. .
“C” Count
C Count (# Frames)
0
15
16
31
A
B
Transfer Configuration
Let's look at a simple example...

## Slide 10: Example – How do you VIEW the transfer?
ACNT = 2
BCNT = 2
CCNT = 3
ACNT = 1
BCNT = 4
CCNT = 3
ACNT = 12
BCNT = 1
CCNT = 1
= 12
8-bit
Let’s start with a simple example – or is it simple?
We need to transfer 12 bytes from “here” to “there”.
What is ACNT, BCNT and CCNT? Hmmm….
You can “view” the transfer several ways:
Which “view” is the best? Well, that depends on what your system
needs and the type of sync and indexing (covered later…)
Note: these are contiguous memory locations

## Slide 11: C6748 – EDMA Channel/Parameter RAM Sets
EDMA3 has 128-256 Parameter RAM sets (PSETs) that contain configuration information about a transfer
64 DMA CHs and 8 QDMA CHs can be mapped to any one of the 256 PSETs and then triggered to run (by various methods)
PaRAM Set 0
PaRAM Set 1
PSET 63
PSET 64
PSET 255
. .
. .
31 0
Options
Source
Destination
CCNT
RSVD
ACNT
BCNT
SRCBIDX
DSTBIDX
LINK
BCNTRLD
SRCCIDX
DSTCIDX
Each PSET contains 12 registers:
Options (interrupt, chaining, sync mode, etc)
SRC/DST addresses
ACNT/BCNT/CCNT (size of transfer)
4 SRC/DST Indexes (bump addr after xfr)
BCNTRLD (BCNT reload for 3D xfrs)
LINK (pointer to another PSET)
. .
63
64 DMA CHs
0
0
. .
7
8 QDMA CHs
Note: PSETs are dedicated EDMA RAM (not part of IRAM)

## Slide 12: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 13: EDMA Example : Simple (Horizontal Line)
myDest:
8 bits
8
9
10
11
loc_8 (bytes)
1
2
3
4
5
6
7
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
8
9
10
11
8
9
10
11
8
9
10
11
Goal:
Transfer 4 elements from loc_8 to myDest
= 4
1 =
Source
ACNT
Destination
BCNT
CCNT
= 1
= &myDest
= &loc_8
DMA always increments across ACNT fields
B and C counts must be 1 (or more) for any actions to occur
Any indexing needed?
Is there another way
to set this up?

## Slide 14: EDMA Example : Simple (Horizontal Line)
myDest:
8 bits
8
9
10
11
loc_8 (bytes)
1
2
3
4
5
6
7
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
8
9
10
11
8
9
10
11
8
9
10
11
Goal:
Transfer 4 elements from loc_8 to myDest
= 1
4 =
= 1
1 =
= 0
0 =
= 1
= &myDest
= &loc_8
Here, ACNT was defined as element size : 1 byte
Therefore, BCNT will now be framesize : 4 bytes
B indexing (after ACNT is transferred) must now be specified as well
‘BIDX often = ACNT for contiguous operations
Why is this a “less
efficient” version?
Source
ACNT
Destination
SRCBIDX
BCNT
DSTBIDX
SRCCIDX
DSTCIDX
CCNT
Notes: Because you’re “lobbing” one byte at a time to the TC… it can transfer 64 bits at a time without blinking.

## Slide 15: EDMA Example : Indexing (Vertical Line)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
myDest:
8 bits
= 1
4 =
= 6
2 =
= 0
0 =
= 1
= &myDest
= &loc_8
Goal:
Transfer 4 vertical elements from loc_8 to a port
loc_8 (bytes)
ACNT is again defined as element size : 1 byte
Therefore, BCNT is still framesize : 4 bytes
SRCBIDX now will be 6 – skipping to next column
DSTBIDX now will be 2
Source
ACNT
Destination
SRCBIDX
BCNT
DSTBIDX
SRCCIDX
DSTCIDX
CCNT
31
32
33
34
35
36
8
14
20
26

## Slide 16: EDMA Example : Block Transfer (less efficient)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
myDest:
16-bit Pixels
16 bits
Goal:
Transfer a 5x4 subset from loc_8 to myDest
= &myDest
= &loc_8
= 2
4 =
= 2 (2 bytes going from block 8 to 9)
2 =
= 6 (3 elements from block 11 to 14)
2 =
= 5
ACNT is defined here as ‘short’ element size : 2 bytes
BCNT is again framesize : 4 elements
CCNT now will be 5 – as there are 5 frames
SRCCIDX skips to the next frame
8
9
10
11
14
15
...
Source
ACNT
Destination
SRCBIDX
BCNT
DSTBIDX
SRCCIDX
DSTCIDX
CCNT
Frame

## Slide 17: EDMA Example : Block Transfer (more efficient)
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
myDest:
16-bit Pixels
16 bits
Goal:
Transfer a 5x4 subset from loc_8 to myDest
= &myDest
= &loc_8
= 8
5 =
= 12 is (6*2) (from block 8 to 14)
(4*2) is 8 =
= 0
0 =
= 1
ACNT is defined here as the entire frame : 4 * 2 bytes
BCNT is the number of frames : 5
CCNT now will be 1
SRCBIDX skips to the next frame
8
9
10
11
14
15
...
Source
ACNT
Destination
SRCBIDX
BCNT
DSTBIDX
SRCCIDX
DSTCIDX
CCNT
Elem 1
Elem 2
Elem 3
Elem 4
Elem 5

## Slide 18: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 19: “A” – Synchronization
An event (like the McBSP receive register full), triggers the transfer of exactly 1 array of ACNT bytes (2 bytes)
Example: McBSP tied to a codec (you want to sync each transfer of a 16-bit word to the receive buffer being full or the transmit buffer being empty).
Frame 1
Array1
Array2
Array BCNT
Frame 2
Array1
Array2
Array BCNT
Frame CCNT
Array1
Array2
Array BCNT
EVTx
EVTx
EVTx

## Slide 20: “AB” – Synchronization
An event triggers a two-dimensional transfer of BCNT arrays of ACNT bytes (A*B)
Example: Line of video pixels (each line has BCNT pixels consisting of 3 bytes each – Y, Cb, Cr)
Frame 1
Array1
Array2
Array BCNT
Frame 2
Array1
Array2
Array BCNT
Frame CCNT
Array1
Array2
Array BCNT
EVTx

## Slide 21: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 22: Indexing – ‘BIDX, ‘CIDX
EDMA3 has two types of indexing: ‘BIDX and ‘CIDX
Each index can be set separately for SRC and DST (next slide…)
‘BIDX = index in bytes between ACNT arrays (same for A-sync and AB-sync)
‘CIDX = index in bytes between BCNT frames (different for A-sync vs. AB-sync)
‘BIDX/’CIDX: signed 16-bit, -32768 to +32767
‘CIDX distance is calculated from the starting address of the previously transferred block (array for A-sync, frame for AB-sync) to the next frame to be transferred.
. .
EVTx
EVTx
EVTx
. .
‘BIDX
‘CIDXA
A-Sync
. .
EVTx
. .
‘BIDX
CIDXAB
AB-Sync

## Slide 23: Indexed Transfers
1
3
9
11
5
7
13
15
1
3
5
7
9
11
EDMA3 has 4 indexes allowing higher flexibility for complex transfers:
SRCBIDX = # bytes between arrays (Ex: SRCBIDX = 2)
SRCCIDX = # bytes between frames (Ex: SRCCIDXA = 2, SRCCIDXAB = 4)
Note: ‘CIDX depends on the synchronization used – “A” or “AB”
DSTBIDX = # bytes between arrays (Ex: DSTBIDX = 3)
DSTCIDX = # bytes between frames (Ex: DSTCIDXA = 5, DSTCIDXAB = 8)
SRC (8-bit)
DST (8-bit)
SRCBIDX
SRCCIDXA
DSTBIDX
DSTCIDXA
Note: ACNT = 1, BCNT = 2, CCNT = ____
(contiguous)
(contiguous)
Notes: CCNT = 4.

## Slide 24: Example – Using Indexing
ACNT = 2
BCNT = 2
CCNT = 3
ACNT = 1
BCNT = 4
CCNT = 3
ACNT = 12
BCNT = 1
CCNT = 1
8-bit
Remember this example? Ok, so for each “view”, fill in the proper SOURCE index values:
Which “view” is the best? Well, that depends on what you are transferring from/to and which sync mode is used.
‘BIDX = 1
‘CIDXA = 1
‘CIDXAB = 4
‘BIDX = 2
‘CIDXA = 2
‘CIDXAB = 4
‘BIDX = N/A
‘CIDXA = N/A
‘CIDXAB = N/A
Note: these are contiguous memory locations

## Slide 25: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 26: EDMA3 Basics Review
Event – triggers the transfer to begin
Transfer – the transfer config describes the transfers to be executed when triggered
Resulting Action – what do you want to happen after the transfer is complete?
Count – How many items to move
  A, B, and C counts
Addresses – the source & destination addresses
Index – How far to increment the src/dst after each transfer
1
2
3
4
5
6
7
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
8
9
10
11
8
9
10
11
T
(xfer config)
E
(event)
Done
A
(action)
Options
Source
Destination
Index
Link Addr
Cnt Reload
Transfer Count
Index
Index
C
Rsvd
A
B
T
(xfer config)
Let's look at triggers (events) and actions in more detail...

## Slide 27: How to TRIGGER a Transfer
There are 3 ways to trigger an EDMA transfer:
1
Event Sync from peripheral
RRDY
XRDY
McASP0
EDMA3
ER
EER
Start Ch Xfr
2
Manually Trigger the Channel to Run
Application
Channel y
ESR
Start Ch Xfr
Set Ch #y;
ER = Event Register (flag)
EER = Event Enable Register (user)
ESR = Event Set Register (user)
3
Chain Event from another channel (more details later…)
Channel x
Channel y
CER
Start Ch Xfr
TCCHEN_EN
TCC = Chy
TCCHEN = TC Chain Enable (OPT)

## Slide 28: Transfer Complete Code (TCC)
TCC is generated when a transfer completes. This is referred to as the “Final TCC”.
TCC can be used to trigger an EDMA interrupt and/or another transfer (chaining)
Each TR below is a “transfer request” which can be either ACNT bytes (A-sync) or ACNT * BCNT bytes (AB-sync). Final TCC only occurs after the LAST TR.
TR
TR
TR
TR
TC Ack
EVTx
EVTx
EVTx
EVTx
TCC
31
18
17
12
Options Reg
TCC
TCCMODE
11
10
0
Ch 0-63
NORMAL
EARLY

## Slide 29: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 30: Generate EDMA Interrupt (Setting IERbit)
EDMA Channels
Channel #
TCINTEN=0
TCINTEN=0
TCINTEN=1
TCINTEN=0
TCC=0
TCC=1
TCC=14
TCC=63
63
.
.
.
1
0
Options
Options
TCC
TCINTEN
20
17 12
EDMA Interrupt Generation
0
0
1
0
IPR
IER0 = 0
IER1 = 0
IER14 = 1
IER63 = 0
IER
EDMA3CC_INT
TCC
Use EDMA3 Low-Level Driver (LLD) to program EDMA’s IER bits
IER – EDMA Interrupt Enable Register (NOT the CPU IER) IPR – EDMA Interrupt Pending Register (set by TCC)
64 Channels and ONE interrupt? How do you determine WHICH channel completed?

## Slide 31: EDMA Interrupt Dispatcher
Here’s the interrupt chain from beginning to end:
Use EDMA3 LLD to program the proper callback fxn for this HWI.
EDMA3CC_INT (#24)
2. Interrupt Selector
HWI_INT5
1. An interrupt occurs
3. HWI_INT5 Properties
4. EDMA Interrupt Dispatcher
Read IPR bits
Determine which one is set
Call corresponding handler (ISR) in Fxn Table
5. ISR (interrupt handler)
void edma_rcv_isr (void)
{
SEM_post (&semaphore);
}
How does the ISR Fxn Table (in #4 above) get loaded with the proper handler Fxn names?

## Slide 32: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 33: Linking – “Action” – Overview
1
2
3
4
5
6
7
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
8
9
10
11
8
9
10
11
T
(xfer config)
E
(event)
Done
A
(action)
Options
Source
Destination
Index
Link Addr
Cnt Reload
Transfer Count
Index
Index
C
Rsvd
A
B
T
(xfer config)
Need: auto-reload channel with new config
  Ex1: do the same transfer again
  Ex2: ping/pong system (covered later)
Solution: use linking to reload Ch config
Concept:
  Linking two or more channels together allows the EDMA to auto-reload a new configuration when the current transfer is complete.
  Linking still requires a “trigger” to start the transfer (manual, chain, event).
  You can link as many PSETs as you like – it is only limited by the #PSETs on a device.
How does linking work?
  User must specify the LINK field in the config to link to another PSET.
  When the current xfr (0) is complete, the EDMA auto reloads the new config (1) from the linked PSET.
1
LINK
Config 0
NULL
LINK
Config 1
reload
Alias: “Re-load” “Auto-init”
Note: Does NOT start xfr !!

## Slide 34: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 35: Reminder – Triggering Transfers
There are 3 ways to trigger an EDMA transfer:
1
Event Sync from peripheral
RRDY
XRDY
McASP0
EDMA3
ER
EER
Start Ch Xfr
2
Manually Trigger the Channel to Run
Application
Channel y
ESR
Start Ch Xfr
Set Ch #y;
ER = Event Register (flag)
EER = Event Enable Register (user)
ESR = Event Set Register (user)
3
Chain Event from another channel (next example…)
Channel x
Channel y
CER
Start Ch Xfr
TCCHEN_EN
TCC = Chy
TCCHEN = TC Chain Enable (OPT)

Let’s do a simple example on chaining…

## Slide 36: Chaining – “Action” & “Event” – Overview
1
2
3
4
5
6
7
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
8
9
10
11
8
9
10
11
T
(xfer config)
E
(event)
Done
A
(action)
Options
Source
Destination
Index
Link Addr
Cnt Reload
Transfer Count
Index
Index
C
Rsvd
A
B
T
(xfer config)
Need: When one transfer completes, trigger another transfer to run
  Ex: ChX completes, kicks off ChY
Solution: Use chaining to kick off next xfr
Concept:
  Chaining actually refers to both both an action and an event – the completed ‘action’ from the 1st channel is the ‘event’ for the next channel
  You can chain as many Chan’s as you like – it is only limited by the #Ch’s on a device
  Chaining does NOT reload current Chan config – that can only be accomplished by linking. It simply triggers another channel to run.
How does chaining work?
  Set the TCC field to match the next (i.e. chained) channel #
  Turn ON chaining
  When the current xfr (X) is complete, it triggers the next Ch (Y) to run
Y
TCC
Ch X
EN
Chain EN
?
TCC
Ch Y
DIS
Chain EN
Done ?
RUN Y

## Slide 37: Example #1 – Simple Chaining
EDMA Chain/Evt
EDMA Interrupt Gen
EDMA Channels
5 = 0
6 = 1
7 = 0
55 = 0
0
1
0
0
IER
IPR
EDMA3CC_GINT
Ch #
55
7
6
5
0
0
1
0
CER
5 = 0
6 = 0
7 = 1
55 = 0
5 = 1
6 = 0
7 = 0
55 = 0
OPT.TCCHEN
ESR
7
0
6
55
Triggered manually by ESR
Chains to Ch #7 (Ch #5’s TCC = 7)
0
0
1
0
CER
OPT.TCC
OPT.TCINTEN
7
0
6
55
Channel #5
Triggered by chaining from Ch #5
Interrupts the CPU when finished (sets TCC = 6)
ISR checks IPR (TCC=6) to determine which channel generated the interrupt
Channel #7
CER = Chain Evt Reg
ESR – Evt Set Reg
TCINTEN = “Final” TCC will interrupt the CPU
TCCHEN = “Final” TCC will chain to next channel
Any Ch can chain to any other Ch by enabling OPT.TCCHEN and specifying the next TCC
Any Ch can interrupt the CPU by enabling its OPT.TCINTEN option (and specifying the TCC)
IPR bit set depends on previous Ch’s TCC setting
Notes:
Notes: Instructor – It is really key here to make sure all the students understand this example from beginning to end. Take it slow and show the entire path and logic. Show how TCINTEN/TCCHEN/TCC interact to give the desired result. Start with the “goal” of Channel #5 and Channel #7. Walk them through the path showing how each option and bitfield helps us attain our goal. Make sure they clearly understand what the fields mean on the right. Then, cover the Notes: section. Once they all understand this example, the next two will be simpler.

## Slide 38: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 39: Channel Sort – “Transfer Config” – Overview
1
2
3
4
5
6
7
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
8
9
10
11
8
9
10
11
T
(xfer config)
E
(event)
Done
A
(action)
Options
Source
Destination
Index
Link Addr
Cnt Reload
Transfer Count
Index
Index
C
Rsvd
A
B
T
(xfer config)
Need: De-interleave (sort) two (or more) channels
  Ex: stereo audio (LRLR) into L & R buffers
Solution: Use DMA indexing to perform sorting automatically
Concept:
  In many applications, data comes from the peripheral as interleaved data (LRLR, etc.)
  Most algos that run on data require these channels to be de-interleaved
  Indexing, built into the EDMA3, can auto-sort these channels with no time penalty
How does channel sorting work?
  User can specify the ‘BIDX and ‘CIDX values to accomplish auto sorting
L0
R0
L1
R1
L2
R2
PERIPH
EDMA
BIDX
CIDX
L0
L1
L2
R0
R1
R2
MEM

## Slide 40: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 41: EDMA Architecture
Evt Reg (ER)
Chain Evt Reg (CER)
Evt Enable Reg (EER)
Evt Set Reg (ESR)
Q0
Q1
Q2
Q3
Queue
PSET 0
PSET 1
PSET 254
PSET 255
TR Submit
Periphs
Completion Detection
Int Pending Reg – IPR
Int Enable Reg – IER
TC0
TC1
TC2
TC3
TC
EDMAINT
CC
EDMA consists of two parts: Channel Controller (CC) and Transfer Controller (TC)
An event (from periph-ER/EER, manual-ESR or via chaining-CER) sends the transfer to 1 of 4 queues (Q0 is mapped to TC0, Q1-TC1, etc. Note: McBSP can use TC1 only)
Xfr mapped to 1 of 256 PSETs and submitted to the TC (1 TR – transmit request – per ACNT bytes or “A*B” CNT bytes – based on sync). Note: Dst FIFO allows buffering of writes while more reads occur.
The TC performs the transfer (read/write) and then sends back a transfer completion code (TCC)
The EDMA can then interrupt the CPU and/or trigger another transfer (chaining – Chap 6)
SCR = Switched Central Resource
. . .
Early TCC
Normal TCC
E0
E1
E63
DATA
SCR
Notes: A TR (transmit request) can be either ACNT bytes (for A-sync) or ACNT*BCNT bytes for AB-sync.
Queues are 16 events deep.
Reference is SPRU966
In the U/G, it does show using watermark and threshold. You have debug visibility into the Queue RAM.
There is a EDMA performance app note. SPRAAG8. This might help answer many questions from students. It is ON their lab workstation and will eventually go onto their USB key.

## Slide 42: EDMA Performance – Tips, References
Spread Out the Transfers Among all Q’s
Programming EDMA3 using LLD (wiki) + examples (see next slide…)
TC Optimization Rules (SPRUE23)
EDMA3 User Guide (SPRU966)
EDMA3 Controller (SPRU234)
EDMA3 Migration Guide (SPRAAB9)
EDMA Performance (SPRAAG8)
Don’t use the same Q for too many transfers (causes congestion)
Break long non-realtime transfers into smaller xfrs using self-chaining
Manage Priorities
Can adjust TC0-3 priority to the SCR (MSTPRI register)
In general, place small transfers at higher priorities
Tune transfer size to FIFO length and bus width
Place large transfers on TCs w/larger FIFOs (typically TC2/3)
Place smaller, real-time transfers on TC0/1
Match transfers sizes (A, A*B) to bus width (16 bytes)
Align src/dst on 16-byte boundaries
References
Notes: "Self-chaining" means that TCC is set to the same value as the channel that is operating. If you are using channel 9 and set TCC to 9 and enable chaining then you are using "self-chaining".
Generally, "self-chaining" will be used, for example, to break a 16384-byte transfer into 16 1024-byte transfers. For this, you would use ITCCHEN=1 but probably not TCCHEN=1, and change the parameters from, say
ABSYNC
ACNT=1024
BCNT=16
CCNT=1
To
ASYNC
ACNT=1024
BCNT=16
CCNT=1
In the first case, one sync event is all that is required to make the whole 16x1024 transfer happen. In the second case, only 1024 bytes will be transferred when a sync event comes in to start it, so an intermediate TCC can be generated to come back and trigger a new sync event to the same channel. This repeats after each 1024 bytes (ACNT) are transferred, then ends if TCCHEN=0.
Another useful example is to actually get a 3-D transfer to occur. Since there is no way for a single sync event to make a 3-D transfer happen (only ASYNC and ABSYNC exist, no ABCSYNC), you can use "self-chaining" to get an new sync event at the end of each ABSYNC set that decrements CCNT. Again, you would use ITCCHEN-1 and TCCHEN-0.
If you link AND chain (to yourself), the link is guaranteed to occur before you chain.

## Slide 43: EDMA3 LLD Wiki…
Download the detailed app note…
Use the examples to learn the APIs…
Notes: "Self-chaining" means that TCC is set to the same value as the channel that is operating. If you are using channel 9 and set TCC to 9 and enable chaining then you are using "self-chaining".
Generally, "self-chaining" will be used, for example, to break a 16384-byte transfer into 16 1024-byte transfers. For this, you would use ITCCHEN=1 but probably not TCCHEN=1, and change the parameters from, say
ABSYNC
ACNT=1024
BCNT=16
CCNT=1
To
ASYNC
ACNT=1024
BCNT=16
CCNT=1
In the first case, one sync event is all that is required to make the whole 16x1024 transfer happen. In the second case, only 1024 bytes will be transferred when a sync event comes in to start it, so an intermediate TCC can be generated to come back and trigger a new sync event to the same channel. This repeats after each 1024 bytes (ACNT) are transferred, then ends if TCCHEN=0.
Another useful example is to actually get a 3-D transfer to occur. Since there is no way for a single sync event to make a 3-D transfer happen (only ASYNC and ABSYNC exist, no ABCSYNC), you can use "self-chaining" to get an new sync event at the end of each ABSYNC set that decrements CCNT. Again, you would use ITCCHEN-1 and TCCHEN-0.
If you link AND chain (to yourself), the link is guaranteed to occur before you chain.

## Slide 44: Outline
Overview
Terminology
Examples
Synchronization
Indexing
Events – Transfers - Actions
EDMA Interrupt Generation
Linking
Chaining
Channel Sorting
Architecture & Optimization
Quiz (No Lab)

## Slide 45: Chapter Quiz
L0
R0
L1
R1
L2
R2
L3
R3
16-bit stereo audio (interleaved)
Use EDMA to auto “channel sort” to memory
L0
L1
L2
L3
R0
R1
R2
R3
ACNT: _____
BCNT: _____
CCNT: _____
‘BIDX: _____
‘CIDX: _____
PERIPH
MEM
Could you calculate these ?
BUFSIZE
Name the 4 ways to trigger a transfer?
Compare/contrast linking and chaining
Fill out the following values for this channel sorting example (5 min):

## Slide 46: Chapter Quiz
Name the 4 ways to trigger a transfer?
Compare/contrast linking and chaining
Fill out the following values for this channel sorting example (5 min):
Manual start, Event sync, chaining and (QDMA trigger word)
linking – copy new configuration from existing PARAM (link field)
chaining – completion of one channel triggers another (TCC) to start
L0
R0
L1
R1
L2
R2
L3
R3
16-bit stereo audio (interleaved)
Use EDMA to auto “channel sort” to memory
L0
L1
L2
L3
R0
R1
R2
R3
ACNT: _____
BCNT: _____
CCNT: _____
‘BIDX: _____
‘CIDX: _____
PERIPH
MEM
2
2
4
8
-6
Could you calculate these ?
BUFSIZE

## Slide 48: EDMA3 Terminology
Frame 1
ACNT Bytes
Array1
Array2
Array BCNT
Frame 2
Array1
Array2
Array BCNT
Frame CCNT
Array1
Array2
Array BCNT
CCNT
Frames
BCNT Arrays
3-dimensional transfer consisting of ACNT, BCNT and CCNT:
ACNT = Array = # of contiguous ACNT bytes (16-bit unsigned, 0-65535)
BCNT = Frame = # of ACNT arrays (16-bit unsigned, 0-65535)
CCNT = Block = # of BCNT frames (16-bit unsigned, 0-65535)
Minimum transfer is an array of ACNT bytes
Total transfer count = ACNT * BCNT * CCNT

## Slide 49: Triggering an EDMA Transfer to Start
Each of the 64 DMA channels can be triggered by any of the following:
Event Triggering (from a peripheral) – EER/ER
Manual Triggering - ESR
Chain Triggering - CER
McBSP 0/1 (REVT0/1, XEVT0/1)
Utopia (UREVT/XEVT)
Timer 0/1 (TEVTLO/HI 0/1)
GPIO (GPINT[15:0])
SRIO (RIOINT1)
VCP2 (VCP2REVT/XEVT)
TCP2 (TCP2REVT/XEVT)
HPI/PCI (DSPINT)
I2C (ICREVT/XEVT)
Each event is tied to a specific DMA channel (e.g. XEVT1 → Ch 14) and can be enabled/disabled via EER register
Evt Reg (ER)
Evt Enable Reg (EER)
Periphs
CPU writes a “1” to the corresponding bit of the Event Set Register (ESR)
Evt Set Reg (ESR)
Chain Evt Reg (CER)
Used to execute multiple TRs upon receipt of a single event
Ex: EVTx triggers Ch0, Ch0 completes and triggers Ch1 (TCC=1)
Chained events are captured in the Chain Event Register (CER)
Note: excerpt from SPRU966 – Channel Sync Events
E0
E1
E63
{6455 values given. Check your datasheet}
Notes: For the Channel Controller (CC), there is a priority between ESR, ER and CER:
#1 – ESR
#2 – CER
#3 – ER
Debug – never see ER get set. It gets set, then cleared very quickly. So, a trick is to clear the EER bit during debug so that you can see the ER bit get set.

## Slide 50: Transfer Complete Code (TCC)
TCC is generated when a transfer completes. This is referred to as the “Final TCC”.
TCC can be used to trigger an EDMA interrupt and/or another transfer (chaining)
Each TR below is a “transfer request” which can be either ACNT bytes (A-sync) or ACNT * BCNT bytes (AB-sync). Final TCC only occurs after the LAST TR.
Final TCC can be generated at either of two different times:
TR
TR
TR
TR
TC Ack
EVTx
EVTx
EVTx
EVTx
TCC
NORMAL mode (after peripheral acknowledgement)
TR
TR
TR
TR
EVTx
EVTx
EVTx
EVTx
TCC
EARLY mode (after submitting the last TR to TC)
31
18
17
12
Options Reg
TCC
TCCMODE
11
10
0
Ch 0-63
NORMAL
EARLY

## Slide 51: OPTions Register Details

## Slide 52: Counter Reload
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 2 |  |  |  |  |  |  |  | 
1 | 2 |  |  |  |  |  |  |  | 
EDMA
Left:
Right:
M
cBSP
What happens when BCNT goes to zero?
There’s a register for this
Src Addr
Dst Addr
McBSP
Left
2
2
20
-18
10
CCNT
BCNTRLD.LINK
2
DST.BIDX.CIDX
BCNT.ACNT

## Slide 53: Outline
MainHighlight
MainNormal
SubHighlight
SubNormal